## Slide 1: SDG 7 in Africa State of Play
Stefano Signore
Head of Unit
DEVCO.C6

## Slide 2
Latest data on primary indicators of global progress toward SDG 7 targets
Notes: According to the latest data, the world is making progress towards achieving SDG 7, but will fall short of meeting the targets by 2030 at the current rate of ambition.
In recent years, pronounced progress in expanding access to electricity was made in several countries, notably India, Bangladesh, and Kenya. As a result, the global population without access to electricity decreased to about 840 million in 2017 from 1.2 billion in 2010. Those still lacking access are increasingly concentrated in Sub-Saharan Africa.
Meanwhile, the population without access to clean cooking solutions totaled almost 3 billion in 2016 and was distributed across both Asia and Africa. The widespread use of polluting fuels and technologies for cooking continues to pose serious health and socioeconomic concerns.
Renewable energy accounted for 17.5% of global total energy consumption in 2016. The use of renewables (i.e., sources of renewable energy) to generate electricity increased rapidly, but less headway was made in heat and transport. A substantial further increase of renewable energy is needed for energy systems to become affordable, reliable, sustainable, focusing on modern uses.
Finally, with respect to energy efficiency, global primary energy intensity was 5.1 megajoules per U.S. dollar (MJ/USD) (2011 purchasing power parity) in 2016. Energy efficiency improvements have increased steadily in recent years, thanks to concerted policy efforts in major economies, including China. However, the global rate of improvement in primary energy intensity still lags behind SDG target 7.3, and estimates suggest that improvements slowed in 2017 and 2018.

## Slide 3
Share of population with access to electricity in 2017
Notes: Thanks to significant efforts across the developing world, the global electrification rate reached 89% in 2017 (from 83% in 2010), still leaving about 840 million people without access.
However, the momentum remained uneven across regions in particular for difficult-to-reach populations, particularly in Sub-Saharan Africa, where many remain without access.
Electrification efforts have been particularly successful in Central and Southern Asia, where 91% of the population had access to electricity in 2017.
Access rates in Latin America and the Caribbean, as well as Eastern and Southeastern Asia, climbed to 98% in 2017. Among the 20 countries with the largest populations lacking access to electricity, India, Bangladesh, Kenya, and Myanmar made the most significant progress since 2010.
Sub-Saharan Africa remains the region with the largest access deficit: here, 573 million people—more than one in two—lack access to electricity. The region is also home to the 20 countries with the lowest electrification rates. Burundi, Chad, Malawi, the Democratic Republic of Congo, and Niger were the four countries with the lowest electrification rates in 2017.

## Slide 4
The 20 countries with the largest access deficit over the 2010-2017 tracking period
Notes: Although India, with 12% of the global access deficit, reached an access rate of 93%, surpassing the global electrification rate, 99 million of its population remained without access to electricity in 2017.
With 16 out of the top 20 countries electrifying at over 1 percentage point each year since 2010, the largest access-deficit countries are also driving the global increase in electrification and progress on SDG indicator 7.1.1.
But, this growth had only a marginal effect on the net decline in the population without access.
Global growth in access was in fact driven by countries like India and Bangladesh, where incremental access outpaced population growth by a significant margin.
Yet, in a majority of the top 20 access-deficit countries, this incremental access between 2010 and 2017 did not keep pace with population growth. Moreover, some of the countries with unserved populations of over 50 million in 2017—like the Democratic Republic of Congo, Nigeria, and Pakistan—have electrified less than 1 percentage point of their population annually since 2010.

## Slide 5
Source: IEA
Population without access to electricity by country in Africa, 2018
Notes: In sub-Saharan Africa 55% of people lack access to electricity;
In thirteen countries, more than three-quarters of the population do not have access to electricity
More than two-thirds of people without access to electricity in the world today live in sub-Saharan Africa.
North Africa reached almost universal access to electricity by 2018, but the electrification rate in sub-Saharan Africa was 45% in that year.
Electrification levels in sub-Saharan Africa remain very low compared to the levels in other developing parts of the world, most notably the 94% rate reached on average across developing countries in Asia.

## Slide 6
Electricity access in the 20 least electrified countries, 2010-2017
Source: World Bank
Notes: The 20 least-electrified countries are concentrated in the Sub-Saharan African region and were home to over 320 million people lacking access to electricity in 2017.
Apart from Burundi, Malawi, Chad, and the Democratic Republic of Congo, these countries have been electrifying at a rate of over 1 percentage point annually since 2010. South Sudan and Rwanda, in particular, stand out for their annual rate of over 3 percentage points.

## Slide 7
Source: WHO 2019
Rate of access to clean cooking fuels and technologies, 2017
Notes: The countries with the largest populations without access to clean cooking fuels are mostly in Sub-Saharan Africa, South and Southest Asia
The top 20 access-deficit countries (in population without access; blue dot on the map) accounted for 82% of the global population without access. India alone still accounts for the largest share of the access deficit at 25%, followed by China at 20%. Put together, India and China accounted for 45% of the total population without access to clean cooking fuels in 2017
Between 2010 to 2017, access did not improve substantially in Sub-Saharan Africa, remained stable in Latin America, and showed only slow process in Developing Asia.
The rate of access to clean cooking solution remains much higher in urban areas, where around 83% have access, than in rural areas, where only 34% have access.

## Slide 8
Analysis of the 20 countries with the lowest access rates to clean cooking fuels
Source: World Bank
Notes: The 20 countries with the lowest access rates to clean cooking fuels are all in Sub-Saharan Africa with very little improvement over the years.
Overall, in the 20 countries where the shares of population with access to clean cooking fuels are the smallest, the annual increase in access between 2010 and 2017 was very small (always less than 0.2%) and a few countries saw rates of access decrease (e.g., Mali, Madagascar, and Chad).

## Slide 9: Population without access to electricity and clean cooking in Africa 2000-2030
Source: IEA
Notes: Full energy access in Africa remains elusive
Despite progress in several countries, current and planned efforts to provide access to electricity barely outpace population growth; efforts for clean cooking need to accelerate even more

## Slide 10
Source: IEA, 2018
Electricity access progress in sub-Saharan Africa
(IEA Stated Policies Scenario)
Notes: Projected progress in the IEA Stated Policies Scenario is most rapid in East Africa, as it moves from a regional access rate of 43% today to more than 70% by 2030.
Progress is also made in West Africa and Southern Africa, where the regional access rates reach over 60% by 2030.
Kenya, Ethiopia, Rwanda, South Africa. Ghana and Senegal are all set to achieve universal access before 2030.
Strong efforts in Nigeria and Côte d’Ivoire result in their rates of access increasing to 80% and more than 90% respectively by 2030.
Countries across Central Africa see limited progress under the IEA Stated Policies Scenario, but there are some bright spots: Gabon and Cameroon both reach more than 90% by 2030.

## Slide 11
Chart: 
| Other developing regions | Sub-Saharan Africa | Other developing Asia | India | Latin America | World
2017 | 0.95556 | 0.43338 | 0.92825 | 0.87468 | 0.95986 | 0.86795
2030 New Policies Scenario | 0.017631 | 0.17251 | 0.053532 | 0.12532 | 0.031989 | 0.055799
2030 SDG gap | 0.026813 | 0.39411 | 0.018223 | 0 | 0.0081481 | 0.076251
Chart: 
| Decentralised renewables | On-grid renewables | Coal | Oil | Gas | Nuclear
Sustainable Development Scenario | 0.51197 | 0.26237 | 0.048321 | 0.048321 | 0.079375 | 0.0089615
Electricity access rates
Least-cost solutions to provide universal access by 2030 in the sustainable development scenario
Source: IEA, 2018
Electricity access rates by region in 2017 and 2030
Least-cost solutions to providing universal access to electricity by 2030
Notes: [LEFT] ELECTRICITY ACCESS RATES
Under current and planned policies, and despite an acceleration of the progress in all world regions, the world is not on track to achieving universal electricity access by 2030, with sub-Saharan Africa at great risk of being left behind.
[RIGHT] LEAST COST SOLUTIONS TO PROVIDE UNIVERSAL ACCESS BY 2030
While since 2000, fossil fuels have been the source of 70% of new electricity access, and the centralised grid for 99% of connections, the IEA’s Sustainable Development Scenario show that achieving universal access in a least-cost way by 2030 would require a complete shift of technologies, taking advantage of the unprecedented cost advantage of renewables, in particular decentralized renewables, to reach the most remote locations.
51% of the 1.2 billion people who should gain access by 2030 could be electrified in a least-cost way through clean decentralized systems; in rural areas, this share reaches 77%.
Grid-based connections are still essential worldwide, as they offer a least-cost solution for 42% of people who need to gain a connection by 2030. Nonetheless, thanks to declining clean technology costs, on-grid renewables surpass fossil fuels in providing people with new connections.

## Slide 12
Top 20 countries with highest rates of electricity access to off-grid supply (tier 1 or higher), 2017
Notes: The African countries with the so far largest efforts in off-grid access are Rwanda (mainly Solar Home Systems,; SHS), Uganda (SHS), Kenya (SHS), Tanzania (SHS), Liberia (mini hydro), Mali (solar mini grids), and Guinea-Bissau (SHS).
Globally, at least 34 million people had access to the equivalent of a minimum basic (tier 1+) electricity service either through SHSs or connection to mini grids based on solar, hydropower and biogas in 2017.
This marks a threefold increase from 2010 – 2017 in the population connected to electricity from off-grid sources.
Population with access to SHS has grown 3.5 times between 2010 – 2017, while population with access to PV mini grids grew 4.5 times between 2010 – 2017.
There is a slowdown in the uptake of Tier 1+ SHS in recent years because of the transition to grids and mini grids in countries such as Bangladesh, but there continues to be an uptick in in several countries including Kenya, Rwanda and Uganda. The share of the population getting access through min grids increased by 16 percentage points between 2015 and 2017. These trends indicate the increasing maturity of off-grid and mini grid markets and technologies, but there is still scope for countries to exploit the full potential of these electricity sources.

## Slide 13
Chart: 
| Other developing regions | Sub-Saharan Africa | Other developing Asia | India | Latin America | World
2017 | 0.97074 | 0.1731 | 0.60655 | 0.47489 | 0.88771 | 0.64677
2030 New Policies Scenario | 0.003063 | 0.21609 | 0.13344 | 0.187 | 0.026236 | 0.096252
2030 SDG gap | 0.0262 | 0.61081 | 0.26001 | 0.33811 | 0.086054 | 0.25698
Chart: 
| Gas | LPG and kerosene | Electricity | Improved biomass cookstoves | Other
 | 92.3683 | 93.8594 | 38.6099 | 122.6635 | 10.6787
Clean cooking access rates
Cooking fuels in developing countries in the sustainable development scenario, 2030
Source: IEA, 2018
Clean cooking access rates in 2017 and 2030
Cooking fuels in the sustainable development scenario, 2030
Notes: [LEFT] CLEAN COOKING ACCESS RATES
On the basis of current trends, 2.2 billion people are still projected to remain without access to clean cooking facilities in 2030, representing 26% of the global population; those are mainly distributed among Asia and Sub-Saharan Africa.
Even though near-universal access to electricity is achieved in Asia, 1.2 billion people are still projected to be without clean cooking access by 2030, with 500 million in India.
In Sub-Saharan Africa, around 900 million people would still rely on polluting fuels and technologies for cooking in 2030.
Despite this slowly falling number, strong population growth hides some success: 900 million people are expected to gain clean cooking access over the period.
[RIGHT] COOKING FUELS IN DEVELOPING COUNTRIES IN SUSTAINABLE DEVELOPMENT SCENARIO
Considering technology costs, historical progress, population growth, urbanization levels, and the availability of fuel, LPG is the predominant solution for urban households by 2030, as population density justifies investment in the necessary LPG infrastructure.
Meanwhile, improved biomass cookstoves are particularly suited for rural areas, where they would represent 34% of fuels used in 2030.

## Slide 14
Source: IEA, UNSD
Change in renewable energy’s share of total final energy consumption between 2010 and 2016
Notes: In 2016, the share of renewables in total final energy consumption increased at the fastest rate since 2012 and reached almost 17.5%.
In 2016, the share of modern renewables (that is, excluding these traditional uses of bioenergy) in total energy consumption reached 10.2%, up from 8.6% in 2010, while the share of traditional uses of biomass declined to 7.3% from 7.9%.
While the RE share increased in several industrialized countries such as the US, EU, Australia Russia and China, the share is currently still decreasing in many developing countries, where fossil fuel based electricity generation as well as the oil-based transport sector are still growing significantly.
The top 20 energy-consuming countries in 2016 were responsible for three-quarters of global energy demand and two-thirds of global renewable energy consumption. In the six countries where consumption of renewables was above the global average, the trend was led by traditional uses of biomass (in India, Indonesia, Nigeria, and Pakistan), modern biomass (in Brazil), or hydropower (Canada).

## Slide 15
Renewable’s share of all energy consumed, by end use, 1990-2016
Notes: Of the three end uses of renewables—electricity, heat, and transport—the use of renewables grew fastest with respect to electricity, driven by the rapid expansion of wind and solar technologies.
The share of renewables in electricity consumption increased by 1 percentage point to 24% in 2016. This was the fastest growth since 1990, more than double that of 2015. It was driven by three key developments: (i) drought recovery in Latin America and an associated increase in hydropower generation, (ii) China’s record-level wind capacity additions in 2015, which became fully operational in 2016, and (iii) rapid expansion of solar capacity in China and the United States. Hydropower remains the largest source of renewable electricity, accounting for 68% in 2016. It is followed by wind, bioenergy, solar, and geothermal.
The share of renewables in heat remains the highest among the three end uses. That share surpassed 24% in 2016, an increase of 0.5% year on year. However, most of the share reflects traditional uses of biomass. Only 9% of heat was generated from modern renewables in 2016.
The share of renewable energy in transport remains lowest: it increased by 0.1% year on year to reach 3.3% in 2016. Biofuels constitute the majority of renewable energy used for transport in the United States, Brazil, and the European Union. Electricity generated from renewable sources also grew, linked to rail and the rapid increase of electric vehicles.

## Slide 16
Electricity demand in Africa, 2018 and 2040 (IEA projections)
Electricity generation in Africa, 2018 and 2040 (IEA projections)
Source: IEA
Notes: [Note: diagram focus is electricity consumption]
According to IEA projections, electricity demand growth potential in Africa is large, primarily from emerging middle classes and productive uses; renewables provide over half of electricity with solar PV becoming the second largest source of generation

## Slide 17
Source: IEA, UNSD, World Development Indicators
Compound annual average growth rate of primary energy intensity, 2010-2016
Notes: Energy intensity improvements were largest in Asia. Between 2010 and 2016, primary energy intensity in Eastern and Southeastern Asia improved by an annual average rate of 3.4%. Similarly, in Central and Southern Asia, the average annual improvement of 2.5% between 2010 and 2016 was above the global average and greater than historic trends. A key factor contributing to this is an increase in energy efficiency driven by concerted policy efforts and economic growth.
Rates of improvement are just below the global average in Oceania, and Northern America and Europe.
Improvement rates are lagging in Latin America and Africa, where absolute levels of energy intensity are less than the global average, reflecting differences in economic structure, energy supply, and access.
More country details:
Recent progress on energy efficiency has been more sustained than historical trends. In 2010-2016, the annual rate of primary energy intensity improvement accelerated in 16 of the world’s 20 economies with the greatest energy demand. China saw the most significant improvement, with India, Indonesia, Japan, and the United Kingdom also recording strong progress.
China has the largest total primary energy supply in the world and the fastest rate of primary energy intensity improvement in the countries analyzed. This is in part linked to China’s modernizing economy and changing structure, where more activity is being undertaken in the less-energy-intensive manufacturing and service sectors. The other important driver has been the Chinese government’s efforts to implement policies to drive improvements in energy efficiency, including codes and standards for appliances, buildings, and vehicles, and mandatory energy efficiency improvement targets for China’s most energy-intensive companies.
India and Indonesia are two other major emerging economies that showed strong rates of improvement in primary energy intensity between 2010 and 2016. In both countries, economic growth, driven by less-energy-intensive manufacturing and service sectors, combined with increased energy efficiency to produce this result.
Similar trends are also observed in Japan and the United Kingdom, which have long implemented energy efficiency policies.
Brazil and Iran are the two major energy-consuming countries where primary energy intensity is worsening. This is linked to stagnant economic conditions in both countries, which have sizeable energy-intensive industry sectors.