## Slide 1
Domingo Zarzo, PhD
Technical and Innovation Manager Sacyr Water
President of AEDyR (Spanish Desalination and Reuse Association)
Member of the BoD of IDA (International Desalination Association)
Desalination
Experience, challenges and future

## Slide 2
The 5 countries with the highest production of desalinated water are the Gulf countries, with Saudi Arabia in the lead, the U.S. and Spain. Currently there are some other countries with important desalination programs such as Australia, Algeria, Chile, etc.
According to recent data, Desalination capacity worldwide is more than 100 million m3/day including around 18,000 installations providing 5% of freshwater.
Desalination in the world
Chart: Desalination by region
| MENA | W EU | Africa | E EU | Nort America | Latam/Carib | South Asia | East Asia
 | 0.47 | 0.1 | 0.02 | 0.02 | 0.12 | 0.06 | 0.03 | 0.18
Source: Juan Miguel Pinto. “Water market trends for LATAM”. Aladyr Majlis Forum IDA World Congress, Dubai, Octubre 2019

## Slide 3
Chart: Distribution of total capacity by raw water origin
| Agua de mar | Agua salobre | Agua de río | Agua residual | Agua pura
 | 59 | 22 | 9 | 6 | 4
Chart: Distribution of installed capacity by technology
| RO | MSF | MED | ED/EDR/EDI | NF/SR | Otros
 | 65 | 21 | 7 | 3 | 2 | 2
Source: IDA Yearbook 2014-2015
Technologies and water origin
Others
Seawater
Brackish water
River water
Wastewater
Pure water
Chart: Distribution of installed capacity by use
| Municipal | Industrial | Centrales eléctricas | Riego | Turismo | Militar | Otros
 | 60 | 28 | 6 | 2 | 2 | 1 | 1
Municipal
Industrial
Power plants
Irrigation
Turism
Military
Others

## Slide 4
HIGH PRESSURE PUMPS AND ENERGY RECOVERY
POST-TREATMENT
PRE-TREATMENT
1) Physical
2) Chemical
SEAWATER INTAKE
STORAGE AND PUMP DISTRIBUTION
RO TRAINS
Seawater desal block diagram
Conventional
Membranes
Physical treatment

## Slide 5
where desalination was born
Egyptian alchemists used apparatus for vaporizing substances, including liquids and seawater
Roman legions used solar distillation for obtaining fresh water in their campaigns in Africa
The ancient Mediterranean
Aristotle (384-322 BC) in his works discussed the nature and properties of seawater and the possibility of its desalination.
Pliny the Elder (23-79 AD), in his great encyclopedia on natural history describes several methods to desalinate water.

## Slide 6
SWRO Prat (200,000 m3/day)
EDR Abrera (200,000 m3/day)
SWRO Torrevieja (240,000 m3/day)
SWRO Aguilas (210,000 m3/day)
BWRO El Atabal (200,000 m3/day)
SWRO Valdelentisco (140,000 m3/day)
SWRO Carboneras (120,000 m3/day)
NF Almoguera (123,800 m3/day)
SWRO Skikda (100,000 m3/day)
SWRO Hamma (200,000 m3/day)
SWRO Fouka (120,000 m3/day)
SWRO Beni Saf (150,000 m3/day)
SWRO Tlemcem (200,000 m3/day)
SWRO Magtaa (500,000 m3/day)
SWRO Hadera (368,000 m3/day)
SWRO Ashkelon (326,144 m3/day)
SWRO Palmachim (110,000 m3/day)
SWRO Soreq (510,000 m3/day)
SWRO Ashdod (384,000 m3/day)
SWRO Mostaganem (200,000 m3/day)
SWRO Tenes (200,000 m3/day)
SWRO Cap Djinet (100,000 m3/day)
NF Mery sur Oise (140,000 m3/day)
PLANT | m3/day
SWRO Soreq (Israel) | 510,000
SWRO Mactaa (Algeria) | 500,000
SWRO Ashdod (Israel) | 384,000
SWRO Hadera (Israel) | 368,000
SWRO Ashkelon (Israel) | 326,144
SWRO Torrevieja (Spain) | 240,000
SWRO Aguilas (Spain) | 210,000
EDR Abrera (Spain) | 200,000
SWRO El Hamma (Algeria) | 200,000
SWRO El Prat (Spain) | 200,000
SWRO Mostaganem (Algeria) | 200,000
SWRO Souk Tleta (Algeria) | 200,000
SWRO Tenes (Algeria) | 200,000
SWRO Tlemcem-Hounaine (Algeria) | 200,000
TOP 10 (14) plants in the Mediterranean Region
Concentration of large plants in the Mediterranean
(26 plants > 100,000 m3/day, 4 brackish, 22 seawater, 1 by EDR)

## Slide 7
Desalination costs include:
O&M:
Manpower
Chemicals
Membrane replacement
Energy
Consumables
Maintenance
Solid waste and environmental costs
Typical Desalination costs (by RO) are between 0.35-0.5 €/m3 (0,6-1,2 €/m3 including payback), depending on plant size, distances between intake, plant and distribution system, with a very strong influence by local manpower and energy prices. For brackish water plants the values are between 0.15-0.3 €/m3.
Cost very influenced by: - productivity factor
- energy costs (40-60%)
Capital costs between 1,200-1,600 €/m3-day installed
Others:
Financial costs
Insurance and guarantees
Desalination costs

## Slide 8
Location | Country | Year | Capacity (m3/day) | Capex | Tariff | Contract
Larnaca | Cyprus | 2001 | 52,000 | 47 M€ | 0.74 US$/m3 | EPC
Ashkelon | Israel | 2005 | 396,000 | 212 MUS$ | 0.52 US$/m3 | BOT
Singspring | Singapore | 2005 | 136,380 | 117 MUS$ | 0.49 S$/m3 | BOO
Honaine | Algeria | 2005 | 200,000 | 225 MUS$ | 0.756 US$/m3 | BOT
Perth | Australia | 2006 | 143,000 | 387 MAus$ | 1.17 Aus$/m3 | DBO
Aguilas | Spain | 2008 | 210,000 | 363 MUS$ | 0.579 US$/m3 | EPC + O&M
Skikda | Algeria | 2009 | 100,000 | 110.8 MUS$ | 0.7398 US$/m3 | DBO
Beni Saf | Algeria | 2010 | 200,000 | 153.4 MUS$ | 0.6994 US$/m3 | DBO
Chennai | India | 2010 | 100,000 | 91 MUS$ | 1.03 US$/m3 | BOT
Limassol | Cyprus | 2012 | 40,000 | 55 M€ | 0.8725 US$/m3 | BOT
SSDP (Perth II) | Australia | 2012 | 306,000 | 601 MUS$ | 0.41 US$/m3 | Alliance
Quingdao | China | 2013 | 100,000 | 135 M€ | 0,71 US$/m3 | EPC + O&M
Tuaspring | Singapore | 2013 | 318,500 | 635 MUS$ | 0.36 US$/m3 | BOOT
Ashdod | Israel | 2014 | 384,000 | 372 MUS$ | 0.538 US$/m3 | EPC
Tenes | Algeria | 2015 | 200,000 | 231 MUS$ | 0.59 US$/m3 | DBO
Tuas III | Singapore | 2018 | 136,000 | 217 MS$ | 0,54 US$/m3 | DBOO
Shuqaiq 3 | Saudi Arabia | 2021 | 450,000 | 600 MUS$ | 0.52 US$/m3 | BOT
Rabigh | Saudi Arabia | 2022 | 600,000 | 650 MUS$ | 0.55 US$/m3 | DBO
Taweelah | UAE | 2022 | 900,000 | 550-1.200 MUS$ | 0.49 US$/m3 | BOT
Capex and Opex of selected large SWRO desalination plants
Desalination costs in large international projects

## Slide 9
Torrevieja 240,000 m3/day
Aguilas 210,000 m3/day
Valdelentisco 180,000 m3/day
3 large plants producing mainly for agriculture
CAPEX (Million €)
293
247
225
Source: Jaime de Miguel , Acuamed.
Cost distribution in large Acuamed desal plants (Spain)

## Slide 10
Francis turbines
Pelton turbines
Isobaric or Hyperbaric systems
CHANGES
Membrane technologies
Unfortunately the thermodynamic limit for salt separation (equivalent to desalination) is approximately 1 Kw-h/m3 for 35,000 ppm TDS)
Thermal processes
(evaporation)
Year | Technology | Kw-h/m3
1970 | MSF | 22
1980 | MSF | 18
1985 | VC | 15
1988 | VC | 13
1990 | RO | 8.5
1994 | RO | 6.2
1996 | RO | 5.3
1998 | RO | 4.8
1999 | RO | 4.5
2000 | RO | 4.0
2001 | RO | 3.7
2002 | RO | 3.5
2005 | RO | 3
2007 | RO | 2.5
Desalination Energy Consumption

## Slide 11
ENERGY SUPPLY
Mumbida Wind Farm near Geraldton 400 Km North of Perth Verve Energy- Macquarie Capital; 22 turbines, 55 MW Greenough River 10 MW Solar Farm (expandable to 40 MW). 80 Has; 150,000 PV panels – largest photovoltaic array in Australia
Southern Seawater Desalination Plant, SSDP), Binningup, Western Australia
Use of renewables in large installations
The use of renewables coupled with desalination is always a target for new facilities but it is difficult for large installations due to a) location, b) footprint and c) continuity (24/7). However it is possible to couple indirectly as in the follow example:

## Slide 12
Environmental aspects
Brine (concentrate) is simply seawater concentrated without any other toxic components
Seawater: 38,000 mg/l TDS
Concentrate: 72,000 mg/l TDS
In Desalination projects is required
- Discharge characterization and marine studies
Environmental impact studies
Discharge alternatives
Discharge dilution model and prediction
Species affection (Posidonia Oceánica)
Environmental monitoring plan (O&M stage)
It is demonstrated that, if the discharge is planned and monitored adequately, the impacts over sea and marine species are irrelevant.
The problem is the discharge inland, without any economically feasible solution.
Current R&D is mainly focused on salt and chemicals production from brines.

## Slide 13
Health aspects
From the Point of view of human health the most important aspect of desalination is the use for drinking water and how it can affect health.
The problem is complex and affects different factors such as:
Water quality: Desalinated water has an excellent quality, free of any kind of pollutants and microbiology but RO permeate has low salinity and needs pH correction and remineralization
All these aspects have been covered and widely developed in a Report by WHO:
“Desalination for safe water supply. Guidance for the Health and Environmental Aspects Applicable to Desalination. WHO/SDE/WSH/07. Public Health and the Environment. World Health Organization, Geneva 2007”
Presence of micropollutants in raw water and how membranes remove them
- Absence of some nutrients (Ca, Mg, etc.)
- Use of chemicals and materials in contact with water

## Slide 14
Uses: desalination for agriculture
Desalination for agriculture is irrelevant globally (< 3%) but countries such as Spain (21%), on the lead, Saudi Arabia, Kuwait or Israel are examples of the use of this application. Desalination for agriculture is feasible for high added value products (mainly in greenhouses and often soil-less). Blending strategies gets feasible prices.
Cuevas de Almanzora Dam
Tajo Segura river transfer
Negratin Dam transfer
Water source | Supply (Hm3/year) | CE (μS/cm) | Water price (€/m3)
Rivers Tajo-Segura transfer | 5.32 | 2,000 | 0.11
Negratin Dam transfer | 5 | 1,300 | 0.23
Subtotal superficial water | 10.32 | 1,661 | 0.17
BWRO Cuevas de Almanzora
Groundwater wells | 1.5 | 3,500 | 0.09
Desalination plant | 4.5 (27.6%) | 300 | 0.34 (*)
Subtotal with desalted water | 16.32 | 1,455 | 0.21
(*) final price includes O&M costs, distribution and management costs
BLENDING STRATEGY CUEVAS DE ALMANZORA (SPAIN) END USERS COMMUNITY

## Slide 15
New technologies and innovation
New technologies:
FORWARD OSMOSIS (FO, PRO, etc.)
PERVAPORATION (PV)
MEMBRANE DISTILLATION( MD)
CAPACITIVE DEIONIZATION (CDI) GRAPHENE
BIOMIMETIC MEMBRANES
AQUAPORINES
MICROBIAL FUEL CELLS
BIOELECTROGENESYS
OTHERS
It is not expected that none of these can replace RO in a medium term. They are installed mainly in laboratory or pilot plants and the future seems for applications such as hybrid processes, brine management or energy production.
Innovation:
Leaving apart the new technologies there are other R&D trends such as:
New membranes and energy recovery devices
Digitalization
Chemicals and salt extraction from brines
Use of drones
Membrane reuse
Use of renewables

## Slide 16
Challenges for the future
To solve the problem with brines inland (to find an economically feasible solution)
Reduction of energy consumption and environmental impacts
Use of renewable energies
Development of new membranes with higher permeability, fouling and oxidant resistance
Prevention and protection against marine events; algae blooms, tsunamis, marine pollution, etc.
Flexibility and management of production and shutdowns
Improve public acceptance of desalination avoiding politicization
Maybe future changes in technologies or hybrid processes
“Small problem”: laws of thermodynamics. Thermodynamic limit for seawater desal: 1 Kw-h/m3
To improve R&D in this field
To promote training: specialized operators and high-quality jobs

## Slide 17
  Zarzo, D., Campos, E., Terrero, P. Spanish Experience In Desalination For Agriculture. Desalination and Water Treatment. Volume 51 (1-3), 53-56 (2013)
  Zarzo, D., Prats, D. (2018). “Desalination and energy consumption. What can we expect in the near future? Desalination 427, 2018, 1-9
  Martinez, V., Soto, M., Lopez de Meneses, J.U., Zarzo, D. (2016). Uso agrario sostenible de agua desalinizada. Agricultura, num. 999, Octubre 2016. Pag. 872-875.
  Burn, S., Hoang, M., Zarzo, D., Olewniak, F., Campos, E., Bolto, B., Barron, O. (2015). “Desalination Techniques – A review of the opportunities for Desalination in Agriculture”. Desalination. Volume 364, p. 2-16, 15 May 2015. Special Issue: Desalination for agriculture
  Barron, O., Riasat, A., Hodgson, G., Smith, D., Qureshi, E., McFarlane, D., Campos, E., Zarzo, D. (2015) “Feasibility assessment of Desalination Application in Australian traditional agriculture”. Desalination. Volume 364, p. 33-45, 15 May 2015. Special Issue: Desalination for agriculture
  Garcia, R., Landaburu, J., Terrero, P., Campos, E., Molina, F., Rabadán, J., Zarzo, D., García-Calvo, E. 2018. Validation of recycled membranes for treating brackish water at pilot scale. Desalination, 433 199-208
  Sola, I., Zarzo, D., Sanchez, J.L. (2019). Evaluating Environmental requirements for the management of brine discharges in Spain. Desalination 471, 114-132
  Sola, I., Sanchez, J.L., Muñoz, P.T., Garcia, E., Saez, C.A., Zarzo, D. (2019). Assessment of the requirements within the Environmental Monitoring plans to evaluate environmental impacts of Desalination plants in Chile. Water, 11, 2085
  Calzada, M., Terrero, P, Campos, E., Buendia, R., Zarzo, D., Maestre, J.F., Gallego, B., Gorriz, B., Alvarez, V., Membibre, P., Valera, D. (2019) LIFE–Deseacrop. Desalinated seawater for alternative and sustainable soilless crop production. IDA World Congress, Dubai, October 2019.
  Buendia, R., Zarzo, D., Garcia, D., Molina, F., Terrero, P., Campos, E., Calzada, M. (2019). Design and construction of a high-energy efficient BWRO desalination plant in the South East of Spain. IDA World Congress, Dubai, October 2019.
  Terrero, P., Campos, E., Calzada, M., Garcia, R., Molina, F., Pomata, D., Lopez, M., Landaburu, J., Garcia, E., Zarzo, D. (2019). LIFE+13 Transfomem: validation of recycled NF and UF membranes in filtration processes. IDA World Congress, Dubai, October 2019.
Some references and more information

## Slide 18
Thank you for your time!
Dr. Domingo Zarzo
dzarzo@sacyr.com