## Slide 1
The Water Team DEVCO C2
05 December 2019
Brussels
What is “new” in the Water sector

## Slide 2
© GCCA/Catherine Paul
We will give a quick look at:
TA Water Facility to help you (and us)…
Different Uses of Sea Water, apart from swimming…
Desalination, what, how, when and how much?
Water harvesting
Underground dams, what?
Cloud seeding
Fog catchment
Faecal Sludge Management, bleah!
The Water Team DEVCO C2
Notes: I

## Slide 3
© GCCA/Catherine Paul
1. Technical Assistance provided by the Water Facility
The Water Team DEVCO C2
Indicative activities
Technical support in programming and preparation of projects
Mobilization of funds, facilitation of partnership
Promotion of industrial and technology cooperation
Contribution to the organisation of EU and other water and sanitation events
Development and promotion of tools contributing to dialogue and coordination of actions in the water sector
Initial stocktaking, technical assistance to establish national Water and Sanitation sector policies
Capacity building in policy and regulatory framework
Development of knowledge and communication tools and products
Water and Sanitation action identification and formulation
Water and Sanitation Dialogue, coordination and exchange of experience
Water and Sanitation knowledge creation, policy elaboration and communication
Key results

## Slide 4
© GCCA/Catherine Paul
2. Different Uses of Sea Water, apart from swimming…
The Water Team DEVCO C2
Technical support in programming and preparation of projects
Mobilization of funds, facilitation of partnership
Initial stocktaking, technical assistance to establish national Water and Sanitation sector policies
Capacity building in policy and regulatory framework
Development of knowledge and communication tools and products
Water and Sanitation action identification and formulation
Water and Sanitation Dialogue, coordination and exchange of experience
Water and Sanitation knowledge creation, policy elaboration and communication
Key results

## Slide 5
© GCCA/Catherine Paul
3. Desalination, what, how, when and how much?
The Water Team DEVCO C2
Initial stocktaking, technical assistance to establish national Water and Sanitation sector policies
Capacity building in policy and regulatory framework
Development of knowledge and communication tools and products
Water and Sanitation action identification and formulation
Water and Sanitation Dialogue, coordination and exchange of experience
Water and Sanitation knowledge creation, policy elaboration and communication
Key results

## Slide 6
© GCCA/Catherine Paul
4.Water Harvesting…
Especially in urban environments, water stress is more and more evident.
In many cases there is abundance of rain, but no water available.
Water Harvesting Potential = rainfall (mm)*collection efficiency
The Water Team DEVCO C2

## Slide 7
© GCCA/Catherine Paul
…runoff waters, how to handle them?
Typical water harvesting system:
The Water Team DEVCO C2

## Slide 8
© GCCA/Catherine Paul
In order to reuse rainwaters/stormwaters, specific norms and standards have be addressed to the way cities are planned and buildings are designed.
Technologies and private sector involvement can accompany and enhance the process and financing
The Water Team DEVCO C2
What do we do with the collected water (1)?
Catchment
Rooftop
Conduit
PVC or other
Filter
Mesh
Storage Recharge
Water stored in tanks (above or below ground, easy)
Groundwater recharging

## Slide 9
© GCCA/Catherine Paul
Criticisms of Artificial Groundwater Recharge
Lack of financial backing and appropriate laws to put land owners in check on the management of drainage wells will lead to break down of the wells. This could further lead to contamination of ground water and clogging of aquifers.
Aquifers can degrade if injected water is not controlled.
Ground water recharge technology might not be as beneficial when small volumes of water are involved. Efficiency is key.
Even though it’s an easy process to understand, adequate knowledge on hydrology is required for a large-scale process.
The Water Team DEVCO C2
What do we do with the collected water (2)?
Catchment
Rooftop
Conduit
PVC or other
Filter
Mesh
Water stored in tanks (above or below ground, easy)
Groundwater recharging
Storage Recharge

## Slide 10
© GCCA/Catherine Paul
If well constructed and maintained drinking water in good quality is available
The Water Team DEVCO C2
5. Sand Dams and Subsurface Dams…
Notes: Difference between subsurface dams and sand dams
Factsheet Block Body
(Adapted from VSF 2006)
As becomes clear from the figures, the general principle of sand storage dams and subsurface dams is similar. In general, sand dams are used when the topographical gradient is high and subsurface dams are used when the topographical gradient is low. If the impervious layer lies near the surface, the storage capacity of the basin will be low. A sand storage dam will enlarge the storage, while a subsurface dam only uses the storage capacity under the surface. When the river is narrow and has high embankments, the storage capacity of a sand storage dam can easily be enlarged. The embankments provide a good anchoring possibility.
Cost consideration
Factsheet Block Body
The cost of an average sand dam with a minimum life span of 50 years and storage of at least 2.000 m3 is about US$ 7.500 (2-4 meters height and 20 meters length; example from Kenya; see case studies in RAIN n.y.). In the case study of Kenya the community covered about 40% of the overall construction costs by being involved in the construction of sand storage dams by provision of labour and raw materials through sand dam management groups (RAIN n.y.).
According to NISSEN-PETERSEN (2006), subsurface dams are less expensive and easier to maintain than sand dams, but do have less capacity. Subsurface dams, basically made out of clay, were constructed in Kenya, with a capacity of 425 to 1342 m3 and at a cost of 900 to USD1600 (VSF 2006).

## Slide 11
© GCCA/Catherine Paul
The Water Team DEVCO C2
Advantages
Storage of seasonal water resources
Protection against evaporation
Reduction of contamination (by livestock and other animals)
Filtration of water flowing through the riverbed sand
Water storage unsuitable for breeding of mosquitoes (malaria) and other insects (compared to open storage)
Inexpensive structures with a high level of community involvement
Disadvantages
The technology is labour and physical capital intensive and most local communities cannot implement it without external aid
A subsurface dam may prevent downstream groundwater flow, and exhausts groundwater in the downstream area
…where and what for???
Notes: Sand dams and subsurface dams (both some times called more general groundwater dams) store water under the ground. A sand dam is a small dam build above ground and into the riverbed of a seasonal sand river. Sand accumulates upstream of the dam, resulting in additional groundwater storage capacity. Similar to sand dam a subsurface dam obstructs the groundwater flow of an aquifer and stores water below ground level. Sand and subsurface dams are suitable for rural areas with semi-arid climate in order to store only seasonal available water to be used in dry periods for livestock, minor irrigation as well as for domestic use. They can be built with locally available material and labour but building a dam still requires relatively high investments, is labour intensive and specific expertise is needed.

## Slide 12
© GCCA/Catherine Paul
6. Cloud seeding? It’s not a joke…
This technology, from 1946, is being increasingly required and used, since it is practically the only way to intensify the availability of fresh water by up to 15%.
The Water Team DEVCO C2

## Slide 13
© GCCA/Catherine Paul
Researchers were able to make drops grow six times faster than normal by copying the insects' shell geometry. Scientists have drawn inspiration from the bumpy shells of Namib desert beetles to improve the collection and transport of water droplets.
The Water Team DEVCO C2
7…after the clouds, the fog?
Santa Monica, CA; 100 M litres/y
Up to 12 litres per m2 per day

## Slide 14
© GCCA/Catherine Paul
…and more examples
The Water Team DEVCO C2
Ethiopia; 80 litres day; bamboo made
Different techniques are adopted, adapted with local materials and technologies; performance is still limited, but in severe water stressed areas can be a potential solution…
Morocco; 150 mm rainfall per year.
1200 people; fog collectors produce 16,000 litres day.

## Slide 15
© GCCA/Catherine Paul
The Water Team DEVCO C2
Kampala, Uganda; digitalisation can help the process to perform better and organise on a demand driven the value-chain
Challenges and difficulties of the Faecal Sludge Management
Strengthening of the legal and institutional framework conditions with clear roles and responsibilities for sector players
Private sector engagement to support the operators in the reform process; business model
Awareness and demand creation among user groups, against taboos
8. And for concluding, before lunch, a nice topic, FSM…

## Slide 16
© GCCA/Catherine Paul
…but why do we have to think to FSM?
Has been calculated that in 15 years, almost 5 billion people will be using on-site sanitation, solutions like pit latrines and septic tanks; what will the world do with all the fecal waste?
The Water Team DEVCO C2
There is much more needed than access to toilets . Safely managed sanitation services is a keystone indicator for ensuring that all people have access to clean water and adequate sanitation. This requires more than just providing households with access to toilets. With very little public money and resources available to physically connect all toilets to public sewer systems, identifying and rolling out cost-effective business solutions for on-site sanitation is more crucial than ever—and holds much promise for improving sanitation globally.

## Slide 17
© GCCA/Catherine Paul
…and thanks for your kind attention!
The Water Team DEVCO C2