## Slide 1: Policies & Concepts 3: Green concept
Roel Slootweg
Day 2 - Session 1

## Slide 2: Natural Green or Sustainability Green ?
Green ‘sensu stricto’: biological (living) environment
  Understand the value of the ecological, economic and social benefits that nature provides (ecosystem services)
  Create ‘natural’ solutions to problems
Green = environmental sustainability
  Green Deal connotation: broadly defined
  Encompassing air, water, soil, climate, biodiversity; i.e. the entire biophysical environment and its linkages with the social environment (underprivileged groups, gender, poverty, …)
  Sustainable production and consumption
this seminar

## Slide 3: Green / Nature-based INFRASTRUCTURE
Green Infrastructure - Enhancing Europe’s Natural Capital (2013) = natural solutions

## Slide 4: Nature-based infrastructure
  Using natural ecosystem processes to address issues traditionally solved by hard (or grey) infrastructure
  Often linked to (but not only) climate resilience and disaster risk reduction
  Considered more flexible / resilient in the light of an unpredictable future
  Combines natural and ‘grey’ solutions: natural where possible, grey where needed
this seminar

## Slide 5: Nature-based INFRASTRUCTURE
Java: permeable structures protect the coast and retain sediments, allowing for mangrove restoration/regrowth (Wetlands International/BwN)
Netherlands Sand Motor: artificial sand bank (21 Mm3) using natural littoral drift for coastal maintenance and providing room for nature and recreation (Building with Nature).

## Slide 6: Greened – Green - Greening
‘Traditional’ project
Sector objectives
Grey design
Assessment:
Avoid, mitigate, compensate
“Do no harm”
‘Greened’ project:
Sector objectives
Re-active green
Assessment:
Retrofitting green elements
“Try to do good”
Enhance, avoid, mitigate, compensate
‘Green’ project:
Sector & green objectives
Pro-active green
Assessment:
“Do good”
Avoid, mitigate, compensate
Business as usual
Greened
Green
re-active
Greening
pro-active

## Slide 7: Greened – Green - Greening
Greening of infrastructure
  Transition of infrastructure design from ‘doing no harm’ to ‘doing good’ for the environment
Greened infrastructure project
  retrofitting green elements into existing grey infrastructure design (re-active greening)
Green infrastructure project
  includes environmental objectives from the onset (pro-active greening)
Greening: re-active ‘greened’ and pro-active ‘green’ projects

## Slide 8: Greened & Green
Animal passages: retrofitting green elements in an already decided upon trajectory.
My home town: legal requirement for water storage => opportunity for water purification, nature and recreation in new housing scheme (+ 30% house value)
preferred

## Slide 9: Climate resilient / climate compatible
Climate resilient infrastructure:
  planned, designed, built and operated in a way that anticipates, prepares for, and adapts to changing climate conditions (includes ecological, institutional, social and engineering resilience) (WB Lifelines)
Climate compatible infrastructure:
  includes both climate-resilient (adaptation) and low-emission (mitigation) infrastructure

## Slide 10
Climate resilient coastal defence:
reduce wave energy and enhance
sand fixation
Climate compatible railway infra:
integrated solar panels
trains operate on wind power
in flood resilient city
at sea
+ hard where
needed

## Slide 11: Biodiversity & Convention
ecosystems
conservation
sustainable use
equitable sharing
species diversity
genetic diversity
BIODIVERSITY IS ABOUT PEOPLE !
3 levels
3 objectives
for
future
use
for equity
between generations
Notes: Ask for familiarity with the levels and objectives. Go through this quickly if needed.

## Slide 12: Biodiversity
  Natural capital: the stock of renewable and non-renewable resources (plants, animals, air, water, soils, minerals)
  Ecosystem services: the flow of benefits that people obtain from ‘nature’ (through provisioning, regulating and cultural services, and supporting services to maintain the flow of other services).

## Slide 13: More information:
ENVIRONMENT & CLIMATE CHANGE MAINSTREAMING FACILITY
EuropeAid-C2-MAINSTREAMING@ec.europa.eu