## Slide 1: Recommendations for ELVs and other conditions setting for petrol stations and terminals
Valts Vilnītis

## Slide 2: EU legal framework
Directive 94/63/EC on the control of volatile organic compound (VOC) emissions resulting from the storage of petrol and its distribution from terminals to service stations
Directive 2009/126/EC on Stage II petrol vapour recovery during refuelling of motor vehicles at service stations

## Slide 3: Latvian example
B category (integrated permits)
  oil depots and terminals with 5000 or more tonnes of fuel per year
  petrol stations with 2000 or more cubic metres of fuel per year
C category (declaration)
  petrol stations with fuel amount of up to 2000 cubic metres per year

## Slide 4: Latvian GBRs
Cabinet Regulation No. 409 (of 12.06.2012.) transposes requirements of the Directives
The GBRs applicable to terminals and stations (both B and C category)

## Slide 5: Latvian GBRs - requirements
Terminals (selected technical requirements)
  Painting the above ground tanks in a colour with a total radiant heat reflectance of 70% or more;
  Tanks with external floating roofs must have primary and secondary seals between the tank wall and the floating roof (95% effectiveness);
  Fixed-roof tanks must either be connected to a vapour-recovery unit or be fitted with an internal floating roof with a primary seal (effectiveness ≥90%);
  Mobile containers which supply petrol to service stations and terminals shall be designed and operated so as to accept and retain return vapours from the storage installations at the service stations or terminals.

## Slide 6: Latvian GBRs – requirements 2
Petrol stations (selected techn. requirements)
  Stage I PVR  if throughput is in excess of 100 m3 per year;
  Stage II PVR  if throughput is in excess of 100 m3 per year and the station is located under living accommodation;
  Stage II PVR  annual throughput is in excess of 500 m3 of petrol.
Notes: Stage I PVR - when petrol is loaded onto tankers and transported to service stations the directive ensures that any vapours are recovered and returned to the tanker or terminal.
Stage II PVR (affectiveness at least 85%) – capture of petrol vapours during refuelling the vehicle fuel tank, and return to tanker.

## Slide 7: Latvian GBRs – requirements 3
Additional requirements relating to soil and groundwater protection
Requirement for baseline report
ELV for vapour recovery units – 35 g/Nm3 (1 hour average)
Other requirements stemming from the Directives and other EU legal instruments

## Slide 8: Conclusions
Latvian GBRs fully transpose requirements of the Directives and apply them to both - integrated non-Annex I permits (B category) and polluting activity declarations (C category)