## Slide 1: Air Quality Governance in the ENPI East Countries
Regulation of non-Annex I activities in the CR and UK
Monika Přibylová

## Slide 2: Air pollution regulation – small pollution sources
Activities not listed in the IPPC law or in the Air protection law:
do not need any air permit, but
have to comply only with general air protection requirements.
Example of these activities:
small boilers with capacity bellow 0,3 MW,
smoking chambers with capacity less than 1000 kg of food products/day,
farms with total yearly emissions of ammonia maximum 5 tons.

## Slide 3: General air protection requirements
Comply with generally prescribed ELV (for 10 substances)
Measure or calculate the amount of the air protection fee and pay it on yearly basis in case it exceeds 2.000 EUR/year.
In combustion sources, it is allowed to use only the fuel for which the source is designed.
Allow environmental inspection or local air protection authorities to check compliance with the air protection regulation.
Combustion sources with heating input from 10 to 300 kW have to make control of the technical state and operation of the boilers for solid fuels, used for production of heat of hot water once per 2 years .

## Slide 4: Generally prescribed ELVs
Polluting substance | Mass flow in g/h | Mass concentration (ELV) in mg/m3
Particulate matter | ≤2500 | 200
 | >2500 | 150
Sulphur oxides expressed as sulphur dioxide | >20000 | 2500
Nitrogen oxides expressed as nitrogen dioxide | >10000 | 500
Carbon monoxide | >5000 | 500
Organic compounds expressed as total organic carbon (TOC), | >3000 | 150
Ammonia and ammonium salts expressed as ammonia | >500 | 50
Hydrogen sulphide, | >100 | 10
Carbon disulphide | >100 | 20
Chlorine and its inorganic gas compounds expressed as HCI | >500 | 50
Fluorine and its inorganic gas compounds expressed as HF | >100 | 10

## Slide 5: Air pollution regulation – medium pollution sources
Specific requirements include:
Operate the source in line with valid air protection permit,
Measure emissions of the source,
Maintain operational records about the source and report the yearly emissions in the integrated reporting system,
Release the emissions to the air by chimney or exhaust tube, unless permitted otherwise,
Remove any hazardous states which can have negative impact on air quality.

## Slide 6: Medium pollution sources - ELVs
The decree no. 415/2012 Coll. sets specific ELV for each category and capacity of these sources. Permit may set stricter ELVs, in case the local environmental conditions require so.
3 additional requirements applicable to some medium polluting sources:
carry out dispersion modelling study (part of the application for air pollution permit or application for permit change),
prepare, follow and update the operational rules of air pollution source,
apply compensation measures in order to eliminate violation of ambient air quality limits.

## Slide 7: Regulation of negligible air polluting activities – no permit
Activities are not listed under Part A or B activities, or are listed under Part B activities, but their operation cannot result in the release into the air of the following substances or there is no likelihood that it will release into the air these substances in a significant quantity.
The determining substances are:
oxides of sulphur and other sulphur compounds;
oxides of nitrogen and other nitrogen compounds;
oxides of carbon;
organic compounds and partial oxidation products;
metals, metalloids and their compounds;
asbestos (suspended PM and fibres), glass fibres and mineral fibres;
halogens and their compounds;
phosphorus and its compounds;
particulate matter.
Notes: This rule does not apply to activities regulated by the EU Solvents emissions Directive or an activity which may give rise to an offensive smell noticeable outside the site where the activity is carried on.

## Slide 8
The permit contains:
ELVs, related reference conditions and monitoring requirements
Other conditions to ensure appropriate preventive measures are taken against air pollution, in particular through application of the BAT and that no significant pollution is caused.
ELVs are specified for the 9 regulated substance, which are likely to be emitted in significant quantities.
If necessary, the permit includes requirements for protection of waters and the soil, and waste management.
Where appropriate, limit values may be supplemented or replaced by equivalent parameters or technical measures.
Regulation of medium air polluting activities in UK – permit

## Slide 9: Emission limit’s benchmarks
no generally binding or applicable ELVs in the UK legislation.
The Environment Agency developed sector specific guidance which contain ELV’s benchmarks achievable by individual types of installations.
These values are the basis for setting ELVs in individual permits for Part B activities.
Link to sector specific guidance:
http://www.defra.gov.uk/industrial-emissions/las-regulations/guidance/