## Slide 1: Emission of pollutants into the atmosphere
Katarina Mareckova ETC ACM , Umveltbundesamt
24 Sept 2012, Chisinau
ENPI workshop

## Slide 2: Content
Introduction
What is NIS and why we need it
Estimation and reporting of emissions
Status of reporting in EECCA

## Slide 3: What is National Inventory System (NIS)
A national inventory system incorporates all the elements necessary
  to estimate,
  report
  and archive emissions (and sinks), i.e.
Legal arrangements
Institutional arrangements
Procedural arrangements
High quality inventory that meets needs of policy-makers, researchers and public
Notes: An NIS is a written account of all arrangements that are needed for preparing and maintaining the inventory. The NIS addresses which institutions (or individuals) do what, what legal systems (formal commitments) need to be in place, and how the inventory preparation should proceed, not just once, but also in following years. The key word is “sustainable.”
The definition of “making arrangements” is preparation or planning. For Parties that have not prepared a comprehensive and sustainable inventory, the NIS would be a detailed and written plan. For Parties that have a sustainable inventory system in place, the NIS would be a detailed and written account of what is now in place and how it needs to be maintained.
NIS is defined in Article 5, par.1, Kyoto Protocol and described in FCCC/CP/2001/13/Add. 3

## Slide 4: Institutional and procedural arrangements
Team coordinator
Sectoral experts
Cooperating institutions
Strategy / workplan in place
QA/QC plan developed
Reporting system in place
Data providers (StatOff, Industies, …
Documentation and Archiving system in place
Leading institution
QA/QC manager
DB manager
Consultants
Research inst.
Universities
Notes: defining tLegal entity: main coordinator/project manager identified
Team of experts with delegated responsibilities established
Cooperating institutions identified and involved in the system (contracts, memorandum of understanding, etc.)
Work plan / Strategy in place
Archiving system established
QA/QC plan developed/implemented
Reporting system in place
  he responsibilities e.g. legal entity responsible for (annual /regular) compilation /reporting of GHG

## Slide 5
Legal arrangements (Act , decree,…)
Ensures resources
Ensures access to inventory data for inventory compilers
Establish system for collecting the data
Define responsibilities (legal entity)
Notes: Legislation in place (Act, Decree,….)
  defining the responsibilities e.g. legal entity responsible for (annual /regular) compilation /reporting of GHG inventories
  ensuring resources
  establishing system collecting the data required for inventory (e.g. National statistical office, Ministries,… )
  providing access to the data for inventory compilers

## Slide 6
Inventory process, Inventory cycle
High quality inventory that meets needs of policy-makers, researchers and public
Inventory Planning
Inventory Management
Inventory Preparation
Assessment of current status
Develop improvement strategy
Notes: An NIS is a written account of all arrangements that are needed for preparing and maintaining the inventory. The NIS addresses which institutions (or individuals) do what, what legal systems (formal commitments) need to be in place, and how the inventory preparation should proceed, not just once, but also in following years. The key word is “sustainable.”
The definition of “making arrangements” is preparation or planning. For Parties that have not prepared a comprehensive and sustainable inventory, the NIS would be a detailed and written plan. For Parties that have a sustainable inventory system in place, the NIS would be a detailed and written account of what is now in place and how it needs to be maintained.
NIS is defined in Article 5, par.1, Kyoto Protocol and described in FCCC/CP/2001/13/Add. 3

## Slide 7: What is an emission, emission source
Releases to air occurring by anthropogenic activities (combustions of fuels, agriculture activities, mining, industrial processes, leakages from equipment's, pipelines…)
Natural emissions (volcano eruptions, forest fires, releases from soil, vegetation,..
Type of source
  Point sources
  Area sources
  Linear sources
  (diffuse emissions)

## Slide 8: Emission estimation
Direct measurements of emissions e.g. from chimney measurements , biogas measurements from landfills, etc…
Estimation by calculation
  Emission factor (mass pollutant per unit activity)
  Activity data
Inverse modeling (e.g. based on air quality measurements)

## Slide 9: Concept of Key categories (80% to national total)
1A1a Public Electricity and Heat Production”,
“1A fi Stationary Combustion in Manufacturing industries and Construction: Other”
“2C1 Iron and Steel Production”.
1A2b Stationary Combustion in Manufacturing Industries and Construction: Non-ferrous Metals
1A4bi Residential: Stationary plants

## Slide 10: Existing reporting formats http://www.ceip.at/reporting-instructions/annexes-to-the-reporting-guidelines/
NFR09 sectors, categories
(E-PRTR activities, UNFCCC CRF categories,…)

## Slide 11: Spatial distribution of emissions
SOx
NH3

## Slide 12: Gridded emissions - Contribution of SNAP (GNFR) sectors to total emissions
S1- Combustion in energy and transformation industries,
S2-Non-industrial combustion plants,
S3-Combustion in manufacturing industry,
S4-Production processes,
S5-Extraction and distribution of fossil fuels and geothermal energy
S6-Solvent use and other product use,
S7-Road transport
S8-Other mobile sources and machinery,
S9-Waste treatment and disposal
S10-Agriculture

## Slide 13: Reporting of LPS

## Slide 14: Quality parameters of emission inventory
T TCCCA
Timeliness
Transparency
Consistency
Comparability
Completeness and
Accuracy
Review process of emissions inventories is established under all Conventions and protocols
  Automated tests on imported of the data
  Semi-automated tests on completeness, consistency
  In-depth review of methods, EF and AD, documentation
Quality control

## Slide 15: Review process under CLRTAP/EEA – T TCCCA
Methods and procedures for the technical review of air pollutant emission inventories reported under the Convention and its protocols (Review Guidelines EB.AIR/GE.1/2007/16)
  Stage 1 - automated tests, Country reports posted on the web during March
  Stage 2 - S&A country reports posted in May http://www.ceip.at/review-results/review-results-2012/
  Stage 3 – Centralised in - depth review of selected inventories
Summary of S1 and S2 findings: In CEIP/EEA technical report Inventory review 2012 http://webdab1.umweltbundesamt.at/download/Reports/2012/InventoryReport2012_forWeb.pdf
Notes: Timeliness, Transparency consistency, comparability , completeness and accuracy

## Slide 16: Review results S1 – S2
http://www.ceip.at/review-results/review-results-2012/
EEA & CEIP report Inventory Review 2012

## Slide 17: Stage 3 in-depth centralized review
Centralized review is review of quantitative and qualitative information of selected inventories by pollutant, country or sector
Joint activity of EMEP/CEIP , EEA and Parties
The work plan is (annually) approved by the EMEP EB
  CEIP
    Coordination of the whole process
    Technical support of ERT
    Communication with Parties
    Publication of final reports
  CEIP/TFEIP/EEA
    Guidance for reviewers, transcripts and templates for review reports
  http://www.ceip.at/review-of-inventories/centralised-review-stage-3/
Notes: Invitations sent out by CEIP by 5 May

## Slide 18: Stage 3 review - long term plan
2013 | Belgium, France , Latvia, Lithuania, Monaco, Norway, Poland, Portugal, Romania, Sweden
2014 | Bulgaria, Cyprus, Denmark, Finland, Hungary, Ireland, Italy, Kazakhstan, Russian Federation, Spain
2015 | Armenia, Azerbaijan, Belarus, Czech rep., Greece, Germany, Netherlands, Slovakia, Slovenia, and Ukraine
2016 | Bosnia and Hercegovina, Croatia, Estonia, Kyrgyzstan, Luxembourg, FYR of Macedonia, Republic of Moldova, Switzerland, United Kingdom and Turkey
2017 | Albania, Austria, Georgia*, EU, Iceland, Liechtenstein, Malta, Montenegro, Serbia

## Slide 19: Assessemnt of IIRs
NIS/ Inst. arrangements
KCA
Completeness info.
Uncertainty info.
Trends explanation
Improvements
Methodology description
Recalculations expl.
Planned improvements
Documentation/ references
Projections
Gridded/ LPS
Transparency / user friendliness
Design
IIR Template
No. of pages
Reporting last 5 years
Reporting 1995-2012
Completeness of data in WebDab

## Slide 20: Assessement of IIRs

## Slide 21: IIR AWARDS 2010-2012

## Slide 22: Reporting of emissions, reporting obligation
LRTAP Convention (21 pollutants: acidifying, ozone precursors, PM, HMs, POPs); 51 Parties
  8 protocols
UNFCCC (GHGs: CO2, N2O, CH4, F-gases) 123 Parties
  Kyoto protocol
Montreal protocol – Ozone depleting pollutants
Aarhus Convention -
  E-PRTR protocol – industrial point sources – 91 pollutants
…….
EIONET framework (EEA) – annual priority data flows
Notes: The European Environment Information and Observation network (EIONET) and EEA

## Slide 23: Data flow
MS inventories
MS inventories
MS inventories
Parties to the CLRTAP
Central DB
UNECE Secretariat
EEA, ETC ACC
RepDab
EMEP SB
modelers
review
Gridded data
inventories
testing
Eurostat
UNFCCC CRF
Surrogate data
Status reports
EMEP EB
Country reports
Notification forms

## Slide 24: Resources for emission inventory compilers:

## Slide 25: Existing Guidance, Guidebooks and Tools
EMEP/ EEA Inventory Guidebook EN and RU http://www.eea.europa.eu/publications/emep-eea-emission-inventory-guidebook-2009
http://www.eea.europa.eu/publications-ru/emep-eea/
EMEP Emission Reporting Guidelines EN and RU ECE/EB.AIR/97 http://www.ceip.at/fileadmin/inhalte/emep/reporting_2009/Rep_Guidelines_ECE_EB_AIR_97_e.pdf
Annexes to the Guidelines I to VI including:
  reporting formats (NFR09 tables)
  IIR template
CollectER emission inventory DB
COPERT road transport software

## Slide 26: Completeness of data in CEIP DB Status as of 1-09-2012
NFR09
NFR02
SNAP
National Total

## Slide 27: Emission trends 1990-2012
Chart: NOx
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Bosnia & Herzegovina
Armenia | 1 | 0.8658 | 0.47186 | 0.2619 | 0.25758 | 0.32251 | 0.24675 | 0.32684 | 0.23701 | 0.22965 | 0.2158 | 0.28855 | 0.27145 | 0.31537 | 0.5094
Azerbaian | 1
Belarus | 1 | 0.051344 | 0.0468 | 0.045793 | 0.052009 | 0.051386 | 0.048598 | 0.053873 | 0.045162 | 0.03942 | 0.03702 | 0.080892 | 0.036908 | 0.035569 | 0.037681 | 0.043505 | 0.042454 | 0.038231 | 0.038384 | 0.041614 | 0.048364
Georgia | 1 | 0.86873 | 0.36911 | 0.25097 | 0.16062 | 0.20541 | 0.38301 | 0.42085 | 0.32703 | 0.23274 | 0.085807 | 0.10859 | 0.114 | 0.12684 | 0.15178 | 0.19704 | 0.2129 | 0.21671 | 0.22039 | 0.2609 | 0.27549
Rep. of Moldova | 1 | 0.74193 | 0.51476 | 0.40538 | 0.35337 | 0.29218 | 0.29065 | 0.27918 | 0.16598 | 0.12934 | 0.20727 | 0.17425 | 0.19086 | 0.23016 | 0.2904 | 0.23694 | 0.1898 | 0.22829 | 0.24192 | 0.21697 | 0.23307
Russian Fed. | 1 | 0.95417 | 0.8675 | 0.84833 | 0.74083 | 0.71389 | 0.68528 | 0.66083 | 0.69111 | 0.69278 | 0.65472 | 0.71278 | 0.78569 | 0.78389 | 0.77639 | 0.93136 | 0.94625 | 0.97 | 0.95173 | 0.65806
Ukraine | 1 | 0.90155 | 0.75661 | 0.6381 | 0.51778 | 0.48405 | 0.42571 | 0.41495 | 0.5082 | 0.49453 | 0.51149 | 0.99437 | 0.53557 | 0.4771 | 0.46446 | 0.46803 | 0.44479 | 0.66719 | 0.75163 | 0.48124 | 0.54983

## Slide 28: Emission trends 1990-2012
Note: Azerbaian and Ukraine did not report.
Chart: DIOX
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Bosnia & Herzegovina
Armenia | 1
Azerbaian
Belarus | 1 | 0.95128 | 0.83987 | 0.70296 | 0.62556 | 0.60876 | 0.64069 | 0.7897 | 0.80172 | 0.73412 | 1.073 | 1.3524 | 1.0513 | 1.2857 | 1.1412 | 1.7022 | 1.2086 | 1.2117 | 1.5427 | 1.6876 | 1.6465
Georgia | 1 | 1.0023 | 0.90648 | 0.80115 | 0.696
Kazakhstan
Kyrgyzstan
Rep. of Moldova | 1 | 0.31393 | 0.25571 | 0.32218 | 0.45262 | 0.38003 | 0.40177 | 0.40626 | 0.44215 | 0.42741 | 0.3832 | 0.2874
Russian Fed. | 1 | 0.9556 | 0.90918 | 0.88597 | 0.83249 | 0.77598 | 0.64279 | 0.61958 | 0.6115 | 0.63068 | 0.63673 | 0.73663
Ukraine

## Slide 29: Emission trends 1990-2012
Chart: PM10
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Bosnia & Herzegovina
FYR of Macedonia
Armenia
Azerbaian
Belarus | 1 | 1.1211 | 1.2593 | 1.3183 | 1.3755 | 1.3457 | 1.2116
Georgia
Kazakhstan
Kyrgyzstan
Rep. of Moldova | 1 | 0.069131 | 0.052778 | 0.082328 | 0.087537 | 0.17204 | 0.11562 | 0.12653 | 0.11476 | 0.12874 | 0.15044 | 0.076658
Russian Fed. | 1 | 1.0253 | 1.1519 | 1.0524 | 1.0919 | 0.92946 | 0.84539 | 0.8617 | 1.0135
Ukraine | 0.024671 | 1 | 1.1067 | 1.1243
Note:, Armenia, Azerbaian and Georgia, did not report.

## Slide 30: Emission trends 1990-2012
Note: Azerbaian and Georgia did not report.
Chart: Hg
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Bosnia & Herzegovina
Armenia | 1 | 1 | 0.8 | 0.9 | 0.1 | 0.1 | 0.08
Azerbaian
Belarus | 1 | 1.0255 | 0.81852 | 0.67145 | 0.55984 | 0.47546 | 0.27642 | 0.28851 | 0.36483 | 0.35366 | 0.33319 | 0.48582 | 0.52612 | 0.56161 | 0.58829 | 0.60402 | 0.66638 | 0.68964 | 0.75758 | 0.85065 | 0.79481
Georgia
Kazakhstan
Kyrgyzstan
Rep. of Moldova | 1 | 1.1302 | 0.97597 | 0.5485 | 0.38179 | 0.2652 | 0.283 | 0.16939 | 0.12044 | 0.053397 | 0.076832 | 0.067042 | 0.11629 | 0.10086 | 0.095817 | 0.072382 | 0.064373 | 0.056363 | 0.071195 | 0.05043 | 0.035598
Russian Fed. | 1 | 0.85897 | 0.73077 | 0.75641 | 0.66667 | 0.66667 | 0.64744 | 0.61538 | 0.60256 | 0.63462 | 0.64103 | 0.65385 | 0.73077 | 0.76282 | 0.89744 | 0.89744 | 0.062821
Ukraine | 1 | 0.23571 | 1.2101 | 0.26314 | 0.23796 | 0.62474 | 0.30169 | 0.27109 | 0.22441 | 0.27097
Datapoint of Armenia in 2007 was 3476%

## Slide 31: Discussion items
How to improve quality of reported emissions
How to ensure /improve communication between data providers and inventory compilers
Where are the problems ?
  AD : accessibility, availability, completeness, confidentiality, …..
  EFs : applicability, uncertainty,….
  Tools: guidance, software, literature, database,..
  Legal barriers,…
  awareness of stakeholders (decision maker, data providers…)
What can we do?