## Slide 1: COPERT 4 Training
2. General Methodology

## Slide 2: Vehicle Categories
Passenger Cars | 
Light Duty Vehicles | 
Heavy Duty Vehicles | 
Mopeds | 
Motorcycles | 

## Slide 3: Vehicle Categories
Passenger Cars
  Gasoline (<1.4 l, 1.4-2.0 l, >2.0 l)
  Diesel (<2.0 l, >2.0 l)
  LPG
Light Duty Vehicles (Trucks & Vans)
  Gasoline
  Diesel
Heavy Duty Vehicles
  Gasoline
  Diesel (11 weight categories)
Power Two Wheelers
  Mopeds (< 50 cc)
  Motorcycles (2-stroke, <250 cc, 250-750 cc, >750 cc)

## Slide 4: Vehicle Categories – Heavy Duty Vehicles

## Slide 5: Vehicle Categories – Rigid Trucks (Lorries)

## Slide 6: Vehicle Categories – Articulated Vehicles
=
+
Tractor
Semi-Trailer

## Slide 7: Vehicle Technologies: Passenger Cars & Light Duty Vehicles
Passenger Cars | Light Duty Vehicles
PRE ECE (~1970 technology) | Conventional
ECE 15/00-01 | LD Euro 1 - 93/59/EEC
ECE 15/02 | LD Euro 2 - 96/69/EEC
ECE 15/03 | LD Euro 3 - 98/69/EC Stage2000
ECE 15/04 | LD Euro 4 - 98/69/EC Stage2005
Improved Conventional | LD Euro 5 - EC 715/2007
Open Loop | LD Euro 6 - EC 715/2007
PC Euro 1 - 91/441/EEC | 
PC Euro 2 - 94/12/EEC | 
PC Euro 3 - 98/69/EC Stage2000 | 
PC Euro 4 - 98/69/EC Stage2005 | 
PC Euro 5 - EC 715/2007 (2010 and on) | 
PC Euro 6 - EC 715/2007 (2015 and on) | 

## Slide 8: Vehicle Technologies: HDVs, Busses, & PTWs
Heavy Duty Trucks/Buses | Mopeds/Motorcycles
Conventional | Conventional
HD Euro I - 91/542/EEC Stage I | Euro 1 - 97/24/EC
HD Euro II - 91/542/EEC Stage II | Euro 2 - 97/24/EC
HD Euro III – 1999/96/EC | Euro 3 – 2002/51/EC (only motorcycles)
HD Euro IV - 2005/55/EC | 
HD Euro V - 2005/55/EC | 
HD Euro VI - 595/2009 | 

## Slide 9: Pollutants – 1(2)
Group 1
Carbon monoxide (CO)
Nitrogen oxides (NOx: NO and NO2)
Volatile organic compounds (VOCs)
Methane (CH4)
Non-methane VOCs (NMVOCs)
Nitrous oxide (N2O)
Ammonia (NH3)
Particulate matter (PM)
PM number and surface area
Pollutants for which a detailed methodology exists, based on specific emission factors
Pollutants which are estimated based on fuel consumption
Group 2
Carbon dioxide (CO2)
Sulphur dioxide (SO2)
Lead (Pb)
Cadmium (Cd)
Chromium (Cr)
Copper (Cu)
Nickel (Ni)
Selenium (Se)
Zinc (Zn)

## Slide 10: Pollutants - 2
Group 3
Polycyclic aromatic hydrocarbons (PAHs) and persistent organic pollutants (POPs)
Polychlorinated dibenzo dioxins (PCDDs) and polychlorinated dibenzo furans (PCDFs)
Group 4
Alkanes (CnH2n+2):
Alkenes (CnH2n):
Alkynes (CnH2n-2):
Aldehydes (CnH2nO)
Ketones (CnH2nO)
Cycloalkanes (CnH2n)
Aromatic compounds
Pollutants for which a simplified methodology is applied, mainly due to the absence of detailed data
Pollutants which are derived as a fraction of total NMVOC emissions.

## Slide 11: General Concept for Exhaust Emissions/Consumption
EHOT [g/veh] = M [km] x EFHOT [g/km]
ECOLD [g/veh] = β x M [km] x EFHOT [g/km] x (eCOLD/eHOT-1)
β = lCOLD/lTOTAL

## Slide 12: What are exhaust emissions dependent on?
Activity
  Number of vehicles [veh.]
  Distance travelled [km/period of inventory]
Hot Emissions
  Technology / Emission Standard
  Mean travelling speed [km/h]
Cold Emissions
  Technology / Emission Standard
  Mean travelling speed [km/h]
  Ambient temperature [Celsius]
  Mean trip distance [km]

## Slide 13: Methodology: Total Emissions
Total Exhaust Emissions: EEXH = EHOT + ECOLD
  Hot (stabilized engine temperature): EHOT = N · M · eHOT
  Cold-start emissions: ECOLD =  · N · M · eHOT · (eCOLD/eHOT-1)
Non-Exhaust Emissions
  NMVOC from Fuel Evaporation: EEVAP = EDIURNAL + ESOAK + ERUNNING
  PM from tyre and brake attrition: EHOT = N · M · ePM

## Slide 14: Non-exhaust emissions (evaporation)
Engine
Fuel Tank
Fuel Line
Canister
Liquid
Vapour
Vent
Breathing Losses
Permeation / Leakages
Mechanisms causing evaporation emissions
  Diurnal emissions
  Hot soak emissions
  Running losses
Parked vehicle
Engine running
Only relevant for Gasoline!

## Slide 15: What is evaporation dependant on
Vehicle technology
Tank (vehicle) size
Canister (vehicle) size
Vehicle mileage (adsorption potential)
Temperature variation
Fuel vapour pressure (kPa)
Fuel tank fill level
Parking time distribution
Trip duration

## Slide 16: Non-exhaust PM
Particulate Matter due to road transport is also produced by:
  Tyre abrasion
  Brake abrasion
  Road wear (not included in COPERT 4)
Emission rates depend on:
  Vehicle category (car, truck, motorcycle)
  Number of axles/wheels (trucks)
  Vehicle load
  Vehicle speed