## Slide 1: COPERT 4 Training
6. GHG Emissions

## Slide 2: Methodology: Algorithm (Diesel)
Fuel Sold (t)
Fossil Diesel
Biodiesel
VKT Travelled
Diesel Vehicles
B30 Busses
Equal fuel mass?
Adjust VKT
RH:C,fossil
RO:C,fossil
Fuel Cons. Factors (g/vkm)
CO2, fossil
CH4, N2O EFs (Tier 3)
CH4, N2O
internal equilibration

## Slide 3: Methodology: Tier Coverage
IPCC Method Coverage by COPERT 4
Legend:
Not Available
NA

## Slide 4: Methodology: CO2 Calculation
Calculation of ultimate CO2 , i.e. all carbon in fuel oxidized to CO2
Operates on the basis of g/km emission factors for consistency with other pollutants
RH:C, RO:C are the ratios of H to C and O to C atoms, respectively in the average fuel molecule

## Slide 5: Internal CO2 correction
Total CO2, fossil
…
…
ΣCO2,calc
CO2 - Diesel cars E1
CO2 - Diesel cars E2
CO2 - B30 Busses
Total CO2,fossil
ΣCO2,calc
CF=
ΣCO2,calc  Total CO2,fossil

## Slide 6: Emission Factors: CO2

## Slide 7: More Info: Petrol CO2
COPERT higher than IPCC Default by ~5%
IPCC absolute value (69 kg/TJ) is low  designates use of oxygenates
European regulations (2009/30/EC) specify 3.7% wt. max oxygen in fuel, i.e. typical Petrol molecule: [CH1.8O0.033]x
Assuming O reduces LHV by 3.3%, then EFCO2 cannot drop below 72 kg/TJ in Europe
Maybe IPCC value dominated by US standards?

## Slide 8: More Info: A closer look to biodiesel
IPCC NCVs - 27 MJ/kg neat biodiesel (B100) - 43 MJ/kg fossil diesel
Extract from Fontaras et al. Environ Pollut 158 (2010) 1451–1460:
Assuming methyl oleate (C19H36O2) as the main ester and IPCC 2006 GL Box 1.1 (grossnet) conversion, the NCVs (MJ/kg) are:
Palm: 37.5, Rape: 37.3, Sunflower 36.2, Fr. Oil: 36.7, Soy: 36.4

## Slide 9: Emission Factors: CH4
Four values (mg/km) are provided: Cold Urban, Hot Urban, Rural, Highway
Data mostly based on ARTEMIS project (2000-2006), values differentiated per vehicle category, Euro standard
Cold/Hot urban part estimated on the basis of cold-start distance
Emission factors for new technologies based on extrapolation. Low CO2 equivalent too weak to justify new measurements.

## Slide 10: Emission Factors: N2O
EFN2O = (aCum.Mileage+b)  EFBASE
  a, b, EFBASE depend on technology level for gasoline PCs & LCVs
  a, b depend on fuel sulfur content
  Different factors for cold urban, hot urban, rural, highway
Much simpler approach for Diesel cars, HDVs and gasoline motorcycles
Note on failed SCR systems

## Slide 11: Recent additions in AEIG/COPERT

## Slide 12: New Fuels
Fuel (m) | Chemical formula | Ratio of hydrogen to carbon | Ratio of oxygen to carbon
Gasoline | [CH1.8]x | rH:C=1.80 | rO:C=0.0
Diesel | [CH2]x | rH:C=2.00 | rO:C=0.0
Ethanol | C2H5OH | rH:C=3.00 | rO:C=0.5
E5 | [CH1.8]x (95%) - C2H5OH (5%) | rH:C=1.86 | rO:C=0.025
E10 | [CH1.8]x (90%) - C2H5OH (10%) | rH:C=1.92 | rO:C=0.05
E85 | [CH1.8]x (15%) - C2H5OH (85%) | rH:C=2.82 | rO:C=0.43
ETBE | C6H14O | rH:C=2.33 | rO:C=0.17
Methanol | CH3OH | rH:C=4 | rO:C=1
MTBE | C5H12O | rH:C=2.4 | rO:C=0.2
Natural Gas | CH4 (95 %)- C2H6 (5 %) | rH:C=3.90 | rO:C=0.0
 | CH4 (85 %)- C2H6 (15 %) | rH:C=3.74 | rO:C=0.0
LPG Fuel A | C3H8 (50 %)-C4H10 (50 %) | rH:C=2.57 | rO:C=0.0
LPG Fuel B | C3H8 (85 %)-C4H10 (15 %) | rH:C=2.63 | rO:C=0.0

## Slide 13: Lube Oil Consumption
Category | Fuel/engine category | Age | kg/10.000 km |  | 
 |  |  | Mean | Min | Max
PC | Gasoline | Old | 1.45 | 0.85 | 2.13
 | Gasoline | New | 1.28 | 0.85 | 1.70
 | Diesel | Old | 1.49 | 0.85 | 2.13
 | Diesel | New | 1.28 | 0.43 | 2.13
LDV | Gasoline | Old | 1.45 | 0.85 | 2.13
 | Gasoline | New | 1.28 | 0.85 | 1.70
 | Diesel | Old | 1.49 | 0.85 | 2.13
 | Diesel | New | 1.28 | 0.43 | 2.13
Urban Buses | Diesel | Old | 8.50 |  | 
 | Diesel | New | 0.85 |  | 
Coaches | Diesel | Old | 1.91 | 1.70 | 2.13
 | Diesel | New | 1.70 | 1.28 | 2.13
HDV | Diesel | Any | 1.56 |  | 
Mopeds | 2-stroke | Old | 10.20 | 6.80 | 13.60
 | 2-stroke | New | 6.80 | 5.10 | 8.50
Motorcycles | 4-stroke | Any | 0.43 |  | 0.85

## Slide 14: Lube Oil Impact
Total contribution 0.2-0.3% for developed countries
Contribution potentially more important for developing countries

## Slide 15: CO2 from Urea Consumption
DIN 70070:
  specifies that urea should be in aqueous solution at a content of 32.5% wt (±0.7%) and a density of 1.09 g/cm3.
  If total commercial urea solution sales are known (UC in litres), then total ultimate CO2 emissions (in kg) are:
  If total urea is not known, this can be assumed 5-6% @ Euro V and 3-4% @ Euro VI of fuel consumption

## Slide 16: SCR Urea impact on CO2
All diesel vehicles assumed Euro 6/VI in 2020, require SCR agent ~ 6% of FC
CO2 and consumption taken from PRIMES 2009 baseline
Notes:

## Slide 17: Export to CRF

## Slide 18: Automatic XML-file creation
Automated procedure to export all years to CRF
CO2 exported only on the basis of fossil fuel consumption
Biodiesel/Bioethanol CO2 is set to 0
CH4 and N2O exports are proportional to fuel consumption, example:
CH4,XML,BIO,DIESEL = CH4,COPERT × FCBIO,DIESEL / FCTOT,DIESEL