## Slide 1: Air Quality Governance in the ENPI East Countries
Training on emission inventories
Nomenclature for reporting
11-12 December, 2013, Tbilisi, Georgia

## Slide 2: Outline
Nomenclature for reporting (NFR)
Changes from NFR 09 to NFR 13
  Changes for all categories
  Changes of NFR categories
Notation keys

## Slide 3: Nomenclature for reporting
The present reporting format (the nomenclature for reporting, NFR) was adopted in 2009 and is referred to as NFR09
The NFR reporting tables are organised for the pollutants and categories defined in the reporting guidelines
The NFR tables include emissions and activity data
The reporting template holds the following sheets
  NFR tables for every year in the time series (1980 – year X-2)
  Additional information (explanation to notation keys, Other categories and basic data for mobile sources)
  Projected emissions (with measures and with additional measures)
  Projected activity data
  Gridded emissions
  LPS emissions

## Slide 4: Changes from NFR 09 to NFR 13 Changes for all categories
HCH has been removed from the NFR template
BC has been added to the NFR template
Changing of NFR codes for a large number of categories
  Some without changes of the sources included
  Others consist of new sources some of which are not included in the GB
The updating of codes is to harmonize with the new Common Reporting Format (CRF) used for greenhouse gas emission reporting to the UNFCCC from 2015

## Slide 5: Changes from NFR 09 to NFR 13 Changes of NFR categories (1)
Combustion in manufacturing industries
  New category
    Stationary combustion in manufacturing industries and construction: Other
Other mobile sources:
  Changed category
    Pipeline compressors → pipeline transport
  New category
    Other transport - other
Industrial processes & Solvents and other product use → Industrial processes and product use (IPPU)
  NFR categories has been changed substantially
  Changed categories
    Decorative coating application & Industrial coating application & Other coating application → Coating applications
  Deleted categories
    Limestone and dolomite use
  New categories
    Magnesium production
    Other industrial processes
    Titanium dioxide production

## Slide 6: Changes from NFR 09 to NFR 13 Changes of NFR categories (2)
Agriculture
  New categories
    Animal manure applied to soils
    Sewage sludge applied to soils
    Other organic fertilisers applied to soils (including compost)
    Crop residues applied to soils
    Indirect emissions from managed soils
    Cultivated crops
    Use of pesticides
Waste
  Change of category
    Wastewater handling has been split to Domestic, Industrial and Other wastewater handling
  New categories
    Biological treatment of waste - Composting
    Biological treatment of waste - Anaerobic digestion at biogas facilities
    Hazardous waste incineration
    Sewage sludge incineration
    Other waste incineration
    Open burning of waste

## Slide 7: Notation keys
UNECE/EMEP explanation | UNECE/EMEP explanation
NA – Not Applicable | The source exists but relevant emissions are considered never to occur.
NE – Not Estimated | Emissions occur, but have not been estimated or reported.
NO – Not occurring | A source or process does not exist within a country.
IE – Included Elsewhere | Emissions for this source are estimated and included in the inventory but not presented separately for this source. The source where these emissions are included should be indicated.
NR – Not Reported | According to paragraph 9 in the Emission Reporting Guidelines, emission inventory reporting should cover all years from 1980 onwards if data are available. However, “NR” (not relevant) is introduced to ease the reporting where emissions are not strictly required by the different protocols, e.g. for some Parties emissions of NMVOCs prior to 1988.
C - Confidential | Emissions are aggregated and included elsewhere in the inventory because reporting at a disaggregated level could lead to the disclosure of confidential information.

## Slide 8: Thank you for your attention