## Slide 1
Workshop on EU Air Quality Policy and the use of Economic Instruments for Sustainable Urban Transport Development
October 21-22, 2014 (Chisinau, Moldova)
Air Quality Governance in the ENPI East Countries
Classification of economic instruments for supporting sustainable urban development

## Slide 2: The large number of mechanisms used by governments and the private sector to achieve reduced emissions can broadly be divided into three gross categories:
How to reduce urban pollution
2
Travel demand management;
Traffic management/engineering; and
Energy efficiency and fuel.

## Slide 3
Travel demand management (1)
3
Congestion charging
Fees are applied to single users based on their actual usage of the road space. Variations regarding infrastructure and vehicle types and time of the day/week can be applied.
Singapore ALS and ERP. London CLCCS.
Depending on technology: Economically "optimal". differentiation of charges among user and vehicle groups. Possibility to change charging policies without need to change infrastructure. Attractiveness to decision makers ("spirit of modernity").
High initial investment. High O&M costs. Need for qualified staff for O&M.

## Slide 4
Travel demand management (2)
4
Parking fees
The parking fees are set at a level that influences the use of individual vehicles in certain areas.
North Sydney Council, Australia.
Relatively easy to apply. Widely accepted by the public. Known technology with many systems on the market.
No leverage on transit traffic. Risk of traffic deviation and relocation of businesses (long run). No direct relation to actual vehicle usage.

## Slide 5
5
Emission oriented tax policies
In many countries fuel is subsidised and parking fees are exempted from fringe benefits. Abandoning these subsidies can discourage car usage. On the other hand tax exemptions on technologies with low emissions can increase their use.
No investment required. Easily applicable at a central level. Does not formally restrict technology choices.
Price elasticities of fuel are usually very small, so the effect on demand can be expected to be low. Parking stands in no relation with actual vehicle usage. An effective tax system has to be existent.
Travel demand management (3)

## Slide 6
6
Car sharing
Several individuals use one vehicle, either on an individual basis or organised through commercial companies.
Several individuals use one vehicle, either on an individual basis or organised through commercial companies.
Relatively easy to apply. Little/no investment necessary. Internet access required.
Requires awareness by participants. Restrictions to individual travel behaviour (loss of flexibility). Potential security and safety issues.
Travel demand management (4)

## Slide 7
7
Company bus services
Companies pick up and return their employees along certain established routes according to working hours.
Siemens Mexico City. BASF Rhine-Neckar area, Germany.
Reduces need for individual transportation. No expenditure for public sector service. Increases punctuality of workers.
Only applicable for larger companies who can afford service. Requires sufficient geographic concentration of employees' homes.
Travel demand management (5)

## Slide 8
8
Park & ride schemes
Special bicycles are offered at highly frequented locations to registered users against a fee and can be returned at dedicated stations.
Vélib Paris, France; Call a Bike, Germany; homeport Prague, Czech Republic.
Relatively easy to apply. Widely accepted by the public. Physical exercise for users. Flexible, low-cost option for “last mile” that complements PT. No need for user to care about O&M. Known technology with many systems on the market. No need for own space for bicycle storage. No need to return to point of departure.
Strongly dependent on weather conditions. Requires users' physical effort. Not viable for longer distances F20. Requires investment and O&M (provider). Cycling infrastructure required.
Travel demand management (6)

## Slide 9
9
Land use planning
By organising residential, commercial and leisure areas in an efficient manner demand for (individual motorised) transport can be reduced structurally and space for adequate facilities reserved. Overall targets are population density and proximity to public transport as well as the attractiveness of NMT.
Ottawa, Canada; Nantes, France; Freiburg, Germany; Manchester, UK; Sheffield, UK.
Sustainable and radical approach. No large financial investments necessary. Possibility to take into account multiple mechanisms at the planning stage.
Requires long-term vision and political support. Necessity for reliable and stable legal framework. Often difficult to apply in a built environment.
Travel demand management (7)

## Slide 10
10
Distance-based vehicle taxes and insurance
Vehicle taxes and insurances are structured according to actual vehicle usage, i.e. high mileage results in higher taxes and insurance premia.
Relatively easily applicable. Usually no investment necessary. Applicable in a centralised manner. Incentive for urban concentration.
Disbenefits to people living in remote areas with a need to travel long distances.
Travel demand management (8)

## Slide 11
11
Access restrictions
Vehicles below certain emission thresholds are categorically not allowed to access city centres.
Environmental zones ("Umweltzonen") in Germany.
- Simple approach which is easily understood - Highly effective when properly enforced.
- May cause higher economic inefficiencies compared to a user charge - No revenue generation - Enforcement costs - Political acceptance issues.
Travel demand management (9)

## Slide 12
12
Rickshaw services (man-powered)
Animal transport
…….
Travel demand management (10)

## Slide 13
13
Separate bus lanes/BRT
Buses drive on separated lanes to avoid traffic congestion. Different options with regards to full/partial separation and engineering solutions.
Metrobús, Mexico City; Transmilenio, Bogotá; Bangkok BRT; Brisbane BRT.
- Increases system reliability and performance compared to conventional bus system - Large travel time savings compared to conventional bus - Relatively easily changeable route structure compared to subway - Potentially low-cost alternative to metro service - Congestion reduction potential - BRT: Improved safety and accessibility to disabled an elder people - Bus lane: Cheap and flexible solution.
- Requires sufficient road space - Higher emissions than electrified MRT - BRT: Crowding out of private (mini-)bus operators (employment effects) - Bus lane: Potential need for more enforcement since lanes physically accessible by other traffic.
Traffic management (1)

## Slide 14
14
Traffic management systems
Coordinated traffic signalling and parking space management can enhance traffic flow and reduce congestion. Intelligent transportation systems further adapt to changing traffic situations and can give surface PT vehicles priority over MIT.
Many cities around the world, e.g. Munich.
Integrated system capable of serving various purposes.
Limited scope for improvement under existing infrastructure conditions.
Traffic management (2)

## Slide 15
15
Traffic signalling - public transport priority
Public transport vehicles have priority over other vehicles at traffic lights. PT vehicles communicate with TMS over radio signals.
Many cities around the world.
Relatively easily applicable where TMS exist. Little investment.
Limited scope for improvement under existing infrastructure conditions. Acceptance by individual vehicle users.
Traffic management (3)

## Slide 16
16
Public transport user information systems
Through detailed and timely information of users, the efficiency of public transport can be increased and users can better plan their trips.
Most public transport systems in developed countries.
Increases the efficiency of existing systems. Electronic systems increase the attractiveness of PT.
Requires investment and O&M. Relatively high complexity of electronic systems.
Traffic management (4)

## Slide 17
17
Integrated fares and ticketing
Different PT entities use one ticketing system to allow end-to-end connexions with one fare and consequently increase user comfort.
German "Verbund"-system.
Increases users' comfort. Does not require major investments. Electronic systems used increase system transparency.
Requires operator coordination. Need to identify acceptable charging system. Technical complexity compared to widely used flat fares.
Traffic management (5)

## Slide 18
18
Separate bicycle lanes
Paved bicycle lanes running in parallel to main roads and are physically separated. Various options are possible regarding separation, e.g. coloured surface or separation stripes, kerb stones, vegetated separation lane, etc.
Sydney, Australia; Copenhagen, Denmark; Bangkok, Thailand and many other cities.
Relatively low investment (depending on actual design) Contribution to road safety Improves traffic flow for both motorised and non-motorised vehicles Can increase users' fitness CO2-neutral mobility.
Requires sufficient road space Appropriate enforcement of cyclist rights necessary (unless effective physical separation) Cycling not an option for all terrain and weather types.
Traffic management (6)

## Slide 19
19
Functional walking facilities
In urban areas many trips are made by walking. Sufficient infrastructure to connect people from their place of residence to basic facilities like shops, social infrastructure, PT access, places of work etc. are therefore essential.
Most northern European cities.
Allow for a safe and reliable last mile. Improve cities' image and quality of life. Increase livelihood of the poor. Reduce separation effect of major roads, rail lines etc. CO2-neutral mobility.
Allow for a safe and reliable last mile. Improve cities' image and quality of life. Increase livelihood of the poor. Reduce separation effect of major roads, rail lines etc. CO2-neutral mobility.
Traffic management (7)

## Slide 20
20
Car-free city centres
Extensive pedestrian areas in city centres where only supply vehicles for local businesses or transport for disabled people are temporarily allowed.
Gent, Belgium. Copenhagen, Denmark. Rotterdam, Netherlands.
Highly beneficial for shopping lanes and touristic locations. Increases options of street and city design. Increased road safety and leisure value.
Requires investment in vehicle access barriers. Need for emergency or supply vehicles to access restricted areas. Can cause bottlenecks in overall city road network.
Traffic management (8)

## Slide 21
21
Car sharing can either be organised on an individual basis, usually between colleagues commuting to work, or through platforms matching supply with demand, usually via the internet. For people regularly using the same route with own vehicles, sharing one vehicle can be beneficial in terms of cost and possibly social factors. This can be achieved by driving intermittently – each participant makes the trip with his own vehicle at his turn and takes the others with him – or if one person does the driving and the others pay for the service.
    Car sharing (1)

## Slide 22
22
The system can be facilitated by companies by matching people living close to each other according to their addresses, but most of the times the groups of car sharers develop on their own since a lot of personal as well as organisational factors are involved in the proper functioning. Companies can also offer preferential parking lots (e.g. closer to work places) for car shares. The offer of dedicated market places is an alternative approach. Nowadays these platforms, such as www.carpooling.co.uk (EU) or www.erideshare.com (US), are internet-based, but phone-based services existed in the past against an administration fee. People offering trips can publish them indicating start and end locations, start time, price, number of free places on the vehicle, etc. and users contact suppliers if they find a matching offer. This service allows for the organisation of regular trips, but is particularly helpful for longer distance and irregular trips since drivers and passengers can agree trips several days in advance via email or phone.
    Car sharing (2)

## Slide 23
23
Examples of carpooling sites in the UK and the USA
Car sharing (3)

## Slide 24
24
People offering trips can publish them indicating start and end locations, start time, price, number of free places on the vehicle, etc. and users contact suppliers if they find a matching offer. This service allows for the organisation of regular trips, but is particularly helpful for longer distance and irregular trips since drivers and passengers can agree trips several days in advance via email or phone.
Car sharing (4)

## Slide 25
25
Pros | Cons
Relatively easy to apply. Little/no investment necessary. | Requires awareness by participants. Restrictions to individual travel behaviour (loss of flexibility). Potential security and safety issues. Internet access required.
Car sharing (5)
Car sharing systems benefit from park & ride schemes and unreliable or expensive PT.

## Slide 26
26
This mechanism refers to the provision of exclusive bicycle lanes physically separated from motorised transport and pedestrians. This increases the safety of cyclists and pedestrians and generally increases the acceptance of cycling in the population. Paved bicycle lanes are either built alongside roads or physically separated from the road surface through coloured marks, kerb stones, or separation walls or fences. At intersections cycling lanes are marked on the crossing road in a similar way as pedestrian crossings. By separating bicycles from other traffic overall safety can be increased which in turn contributes to user acceptance. Since average trip lengths are relatively short (around 11,5 km in Europe according to Eurostat, 2007) there is a high potential for a transfer of MIT or PT trips to cycling.
    Separate bicycle lanes (1)

## Slide 27
27
As cycling is (except for the production of bicycles and spare parts) emission free, the emission reduction potential is very high. According to estimates of the Stern Review on the Economics of Climate Change 4.9 pence and 31.6 pence of costs to society could be saved per car kilometre for petrol engines and diesel engines removed respectively in urban agglomerations (far lower values in rural areas). Bicycle lanes at intersections
    Separate bicycle lanes (2)

## Slide 28
28
Further to environmental benefits, there are strong impacts on health and congestion. According to Cycling England (2007), an independent expert body established by DfT in 2005, (quote): Physical activity reduces the risk of developing major chronic diseases (e.g. coronary heart disease, stroke and type 2 diabetes) by up to 50%, and the risk of premature death by about 20-30%; Based on the risk factors for chronic diseases and levels of inactivity it is estimated that the value of reducing these risk factors is £11.16 a year for those under 45 and £99.53 a year for those between 45 and 64. Other similar models have used values of £123 a year (Sustrans and DfT model). While there are studies that even estimate higher benefits of cycling (or disbenefits for not doing so), it is obvious that integrating cycling and walking (instead of driving) in day-to-day activities can make a huge difference for each individual and for society as a whole. With regards to congestion Cycling England (2007) estimates that “if a cyclist makes 160 trips a year of 3.9km, rather than take a car, this would equate to savings for other road users of £137.28 a year as a result of reduced congestion in urban areas and £68.64 in rural environments”.
    Separate bicycle lanes (3)

## Slide 29
29
Pros | Cons
Relatively low investment (depending on actual design). Contribution to road safety. Improves traffic flow for both motorised and non-motorised vehicles. Can increase users' fitness CO2-neutral mobility | Requires sufficient road space. Appropriate enforcement of cyclist rights necessary (unless effective physical separation). Cycling not an option for all terrain and weather types.
    Separate bicycle lanes (4)
Bicycle parking spaces (closed or open) can improve the acceptance of cycling as a means of NMT and reduce the problems users face. Also, spaces for bicycle on PT vehicles facilitate inter-modality in public passenger transport. Furthermore, maps of bicycle routes help users find the most convenient ways to their destination.

## Slide 30
30
The actual choice of mechanisms should always be taken in line with overall urban transport policy targets and has to take into consideration the current and planned/expected future infrastructure and service needs and availability. Choosing a good mechanism in the wrong circumstances is a bad choice. The policy on emissions reduction will have to be set within the context of competing targets like the availability of technologies, the costs, the acceptance by society, the benefits/effectiveness of the mechanisms under given conditions, the interrelations between mechanism bundles, etc.
    Conclusion (1)

## Slide 31
31
When reducing emissions in the context of urban passenger traffic, the overall idea should always be to get individual motorised (fossil fuel) traffic off the road – where no alternative to motorised transportation exists – and make use of economies of scale by introducing larger transportation units under acceptable load factor conditions. Doing so will normally result in a win-win situation with reduced overall cost of service provision, reduced cost to other traffic participants due to less pollution and congestion, reduced infrastructure capacity needs compared to MIT based on conventional cars.
    Conclusion (2)

## Slide 32
32
Reducing emissions always has to do with behavioural changes. Consequently, strong political support and the development of clear strategies on national or city level are a key success factor. On the other hand changes can be introduced on smaller organisational or individual levels. Both spheres are important and have to be motivated or – as is the case with many behavioural changes - enforced. Functional technical inspection and legal enforcement based on sound technical standards and a clear and stable legal framework support the implementation of emission reduction mechanisms. At the same time a lot can be achieved through awareness raising, education, and training – especially since inspection and enforcement cannot completely control human behaviour.
    Conclusion (3)

## Slide 33: Thank you for your attention. Any questions?