## Slide 1
Pacific – Regional Water and Energy seminar, exchange of best practice
14th May, Nadi, Fiji
Up-scaling Sanitation in the Pacific

## Slide 2
Up-scaling Sanitation
Impacts on Public Health, Economic Development and the Environment
Access to “Improved Sanitation”
Bottlenecks for Up-scaling Sanitation in Kiribati
Theory of Change for Up-scaling Rural Sanitation
Creating Demand
Strengthening Supply
Enabling Environment
Knowledge and Learning
Lessons and Next Steps
EU EDF10 KIRIWATSAN Project

## Slide 3: What is the Greatest “Medical Advance” since 1840?

## Slide 4: Life-saving interventions: Improved sanitation
Kiribati has one of the lowest rates of access to improved sanitation and
highest under-five deaths due to pneumonia and diarrhoea

## Slide 5: Open Defecation in Pacific Islands
Fiji, Niue, Tokelau, Tonga, Palau: 0% Open Defecation
Access ● Status ● CATS ● Policy ● CLTS ● Lessons learned
54 %
36 %
Rural
Solomon Islands: 66%
Kiribati: 49%

## Slide 7: 42% of i-Kiribati are children
Chart: 
| Children (0-17 years) | Adults (18-59 years) | Elderly (60+ years)
 | 43782 | 53625 | 5651
42%
52%
43,782 children
(0-17 years)
53,625 Adults
(18-59 years)
5,651 Elderly
(60+ years)
Source: Census 2010

## Slide 8: Why are under-five children dying?
Chart: 
| Pneumonia | Diarrhoea | Malaria | AIDS | Measles | Injuries | Other neonatal causes* | Other
Kiribati | 20 | 9 | 0 | 0 | 0 | 9 | 31 | 31
* Other neonatal causes excludes deaths due to pneumonia and diarrhoea during neonatal period.
Source: UNICEF 2013
%-distribution of causes of death in Kiribati, 2012
Under-nutrition is a contributing factor for many deaths due to infections such as pneumonia and diarrhoea

## Slide 9: Diarrhoeal deaths declining in Kiribati
Chart: Diarrhoeal deaths per 100,000 people
| 1990 | 1995 | 2000 | 2005 | 2010
Children under5 | 268.76 | 178.4 | 81.72 | 53.52 | 43.39
Femals | 89.66 | 67.97 | 32.53 | 22.83 | 20.82
Males | 113.51 | 82.13 | 36.25 | 23.85 | 20.93
Both | 101.97 | 75.23 | 34.43 | 23.35 | 20.88
Access ● Status ● CATS ● Policy ● CLTS ● Lessons learned
Source: IHME

## Slide 10: Child mortality still very high compared to other Pacific Island Countries
Under-five mortality rate: Probability of dying between birth and exactly five years of age, expressed per 1,000 live births
Progress: Kiribati reduced its under-five mortality rate from 94 deaths per 1,000 live births in 1990 to 60 in 2012 (decline of 36%)
The estimated annual number of under-five deaths dropped from 230 in 1990 to 141 in 2012.
Chart: Under-five mortality rate by country, 2012
| Cook Islands | Tonga | Samoa | Vanuatu | Palau | Fiji | Niue | Tuvalu | Solomons | Nauru | RMI | FSM | Kiribati | PNG
 | 10.6 | 12.8 | 17.8 | 17.9 | 20.8 | 22.4 | 25.1 | 29.7 | 31.1 | 37.1 | 37.9 | 38.5 | 59.9 | 63
Source: UN IGME 2013

## Slide 11: Sanitation Access Kiribati

## Slide 12: Economic Costs of Inadequate Sanitation
Kiribati is off track on Millennium Development Goals
  MDG 4 to reduce infant mortality & MDG 7 environmental sustainability
Underinvestment in water supply and sanitation infrastructure, and inadequate operations and maintenance
High rates of open defecation, with around 60% of the population reportedly using the beach, ocean, or lagoons
Total annual economic burden of poor water and sanitation on South Tarawa is estimated to be A$3.7–A$7.3 million
Annual economic cost of A$553-A$1,083 per household, or 2%–4% of the country’s nominal 2013 Gross Domestic Product
Girls have a higher likelihood of suffering from diarrhea and dysentery than boys
Households with no latrines are more likely to suffer from diarrhea and dysentery and in villages with high rates of open defecation
Source: ADB, 2014
Notes: Kiribati is off track in meeting Millennium Development Goal 4, to reduce infant mortality; and 7, to ensure environmental sustainability.
Underinvestment in water supply and sanitation infrastructure, and inadequate operations and maintenance.
Only a small portion connected and in unsewered areas, the use of onsite sanitation options such as septic tanks or pit latrines have resulted in groundwater pollution.
High rates of open defecation, with around 60% of the population reportedly using the beach, ocean, or lagoons.
The total annual economic burden of poor water and sanitation on South Tarawa is estimated to be A$3.7–A$7.3 million. These costs include those borne by the government and households and the wider economy as a whole. This translates into an annual economic cost of A$553-A$1,083 per household, or 2%–4% of the country’s nominal 2013 Gross Domestic Product.
Female children have a higher likelihood of suffering from diarrhea and dysentery than males. Individuals who live in households with no latrines are more likely to suffer from diarrhea and dysentery. Similarly, illness was found to be higher among households located in villages with high rates of open defecation.

## Slide 13: Environmental Consequences

## Slide 14: Bottlenecks to up-scaling rural sanitation
Experiences from the water supply improvement project on Kiritimati (AusAID) 1998-2000 and the Outer Islands Community Water Supply Project in the 1990s (UNCDF).
Supply and Donor driven
Technology focused ~ Hardware vs behaviour
Lack of community engagement and demand
lack of an effective maintenance program, trained operators and community ownership
No link to policy framework
No model for replication and up-scaling
Limited options for low-cost latrines

## Slide 15
Doing the Things Right?
Doing the Right Things?

## Slide 16: The Islands of Kiribati

## Slide 17: Gilbert Island Group

## Slide 18: EU EDF 10 KIRWATSAN Project
16 Outer Islands
70 villages
Phase I 2011-2016 UNICEF 3.2 M Euro
Phase II 2014-2017 SPC/SOPAC 3.3 M Euro
2011
2012
2013
2014
2015
2016
2017
Result 1: Availability and adequacy of groundwater and rainwater ascertained and appropriate water and sanitation systems designed
Result 2: Increased volume of rainwater safely harvested, stored and used
Result 3: Enhanced capacity to install and sustain improved water and sanitation systems

## Slide 19: Framework for Up-scaling Rural Sanitation
Strengthening Supply
Enabling Environment
Knowledge and Learning
Generating Demand
After: Up-scaling Rural Sanitation, World Bank/Water and Sanitation Programme (2012)

## Slide 20
CATS is an umbrella term developed by UNICEF to encompass a wide range of community-based sanitation programming (including Community Led Total Sanitation (CLTS).
Community Approaches to Total Sanitation (CATS) aims to eliminate open defecation in communities around the world.
The CATS ‘Essential Elements’ are the common foundation for UNICEF sanitation programming globally.
Community Approaches to Total Sanitation
Creating Demand

## Slide 21: Generating Demand: CLTS, a new approach in the Pacific

## Slide 22: Triggering Process

## Slide 23: Getting onto the sanitation ladder through local champions

## Slide 24: New access but ‘Improved’ or ‘Unimproved’?

## Slide 25: Community mobilization and capacity building
Approach for community mobilisation and engagement through Community Led Total Sanitation
90 villages on 10 Outer Islands have declared themselves as Open Defecation Free
CLTS triggering in 112 villages and post-triggering to be continued over next 2 years under KIRIWATSAN
Additional training and community visits under GoK funding and expansion to South Tarawa
H.E. President Anote Tong declared his aim to achieve Kiribati Open Defecation Free by 2015

## Slide 26: North Tarawa Open Defecation Free?

## Slide 27: Strengthening Supply
Supporting Supply
Source: Water and Sanitation Program, World Bank, Up-scaling rural sanitation (2012)

## Slide 28: Limited Technology Options for Atoll Environments

## Slide 29: “Technology-based” Sanitation Ladder
Dry Systems
Composting Toilet
Ventilated Improved Pit Latrine
Pit Latrine
Wet Systems
Sanitary Well
Septic Tank and Soakage Trench
Water Seal atrine
Simple to complex wastewater treatment systems in a Traditional Sanitation Ladder

## Slide 30: “Functionally-based” Menu of Options
Dry Systems
Composting Toilet
Ventilated Improved Pit Latrine
Pit Latrine
Wet Systems
Sanitary Well
Septic Tank and Soakage Trench
Water Seal Latrine

## Slide 31: Marketing new options: The ISY toilet

## Slide 32: Local adaptation

## Slide 33: Tested Results

## Slide 34: Sanitation and Hygiene Marketing

## Slide 35: Community Awareness and Engagement

## Slide 36: Enabling Environment
Access ● Status ● CATS ● Policy ● CLTS ● Lessons learned
Enabling Environment

## Slide 37: Knowledge and Sharing
Knowledge and Sharing

## Slide 38: Tracking Progress
Kiribati: Sanitation Output Tracker |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Last updated date: |  |  |  | #######
The output tracker will be tracking input/output indicators from the log-frame. Data will be collected by field monitoring staff and analyzed and reported by the KIRIWATSAN PMU team on monthly basis. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Overall |  |  | Total to 2014 | 2014 Progress |  |  |  |  |  |  |  |  |  |  |  | 
Program Purpose | No. | Outcome Indicator | Baseline | As of | Target |  | J | F | M | A | M | J | J | A | S | O | N | D | Total 2014
Increased access to safe and sustainable water and sanitation all year round and reduced WASH-related diseases in at least 70 out of 139 villages in 16 of the Gilbert group of islands in Kiribati. | 1 | Number of villages increased the access to improved sanitation from 2010 | 0 | 2010 | 70 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2 | Number of villages declared as open defecation free report a decrease in the incidence of diarrhea | 0 | 2010 | 70 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Overall |  |  | Total to 2014 | 2014 Progress |  |  |  |  |  |  |  |  |  |  |  | 
Result area | No. | Result Indicator | Baseline | As of | Target |  | J | F | M | A | M | J | J | A | S | O | N | D | Total 2014
R3. Enhanced capacity to install and sustain improved water and sanitation systems. | 3.2 | Number of Facilitators and Trainers, awareness and CLTS replication | 0 | 2010 | 200 | 73 |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3.3a | Number of villages triggered for CLTS | 0 | 2010 | 70 | ? |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3.3b | Number of villages declared ODF | 0 | 2010 | 70 | ? |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3.4 | Number of villages actively engaged in WASH through Village Welfare Committees and/or Water and Sanitation Committees | 0 | 2010 | 70 | 70 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Overall |  |  | Total to 2014 | 2014 Progress |  |  |  |  |  |  |  |  |  |  |  | 
 | No. | Indicators | Baseline | As of | Target |  | J | F | M | A | M | J | J | A | S | O | N | D | Total 2014
Triggering Demand requires pro-active follow-up
CLTS Monitoring, Verification and Certification
Provision of community support

## Slide 39: Still interested…

## Slide 40: CLTS Works… but will be not enough on its own!

## Slide 41: Next Steps for KIRIWATSAN
Roll out of CLTS post triggering to 70 villages in 16 Gilbert Islands and possibly Kiritimati island
Recognition of CLTS as Key Strategy to eliminate open defecation and increase access to improved sanitation
Develop targeted training manuals and guidelines
Support communities to move up the Sanitation Ladder
Develop appropriate guidelines and a menu of options for on-site sanitation improvements
Address risks of groundwater pollution through drinking water safety planning and sanitary surveys
Develop policy guidance on provision of subsidies or incentive schemes
Increase National monitoring, verification and certification of ODF status
Link Community Approaches to Total Sanitation with Sanitation Marketing
Sustain efforts through WASH in Schools programmes

## Slide 42: Synergy between WASH Programs
Increasing Access to Water and Sanitation
EU/UNICEF/SPC
Sanitation Improvement Project
ADB
Community Led Total Sanitation
UNICEF/ESR
On-site Sanitation technology trials and studies on groundwater impacts
EU EDF10 KIRIWATSAN I + II
New Zealand Partnerships for Development Fund
Project 43072 South Tarawa Sanitation Improvement Project
Regulatory framework and incentive schemes
Community Mobilization, Water and Sanitation Assessments, Capacity Building

## Slide 43
END