## Slide 1: Challenges of Urbanisation for Sanitation Infrastructure in Lesotho
By :
Palesa Monongoaha
Project Manager - WASCO

## Slide 2
CONTENT
  WASCO’S Mandate
  Impact of urbanisation on sanitation infrastructure
  Current Service levels
  Policy Gaps for connections to sewerage
  Future Strategies/key questions to be addressed by National Sanitation Policy

## Slide 3
WASCO’s Mandate
The Water and Sewerage company is mandated to provide potable water and to collect and treat wastewater in all the designated urban centres of Lesotho

## Slide 4
  Impact of urbanisation on provision of sanitation infrastructure

## Slide 5
Migration from the Rural to the Urban areas
  In accordance with the National Census, there has been a increase in migration from the rural to the urban areas
  In 1996 there were an estimated 250,000 People in Maseru and that number has increased to approximately 350,000 in 2006
  The impact of urbanisation has been an increase in the demand for services, sanitation included

## Slide 6
Rapid development of settlements
  Settlements have developed at a rapid pace and provision of services has not matched this rapid development
  Services are being provided in already settled areas resulting in projects that are more expensive and difficult to implement
  Large areas are in some cases left unserved due to encroachment of private properties on service corridors

## Slide 7
Settlement patterns
  Our settlements are such that different income groups settle together
  We have a mixture of high income, middle income and low income households
  Provision of sanitation services in these mixed settlements requires a mixture of technologies taking into account the ability of households to pay for these services.

## Slide 8
Settlements Cont’d
  Most of our settlements are not planned and in most cases there are no corridors left for services.
  This leaves us with no choice but to lay sewer lines inside the road reserve
  Whilst this is a normal practice in the world, it comes with a number of challenges in settled areas which include:
    Disruption of services (water, electricity, telecommunication)
    Access issues to individual plots
    The requirement to obtain permission from other authorities (Roads Directorate, Maseru Municipal Council)

## Slide 9
Competition between water supply and sanitation
  The focus in terms of resource allocation has always favoured water supply
  In the process, a large backlog has been created which requires a lot of resources to bring sanitation provision up to par with water supply

## Slide 10
Current Situation
  On water supply, WASCO has three levels of Service
    In-house connections
    Tap-in-yard
    Stand pipes

## Slide 11
  The company has 47084 water connections classified into:
    Domestic and
    Non-domestic
    And 106 stand pipes
    Country-wide the
    Majority of which are
    In Maseru (39)
Chart: Water Connections
| Domestic | Non-Domestic | Stand pipe
 | 44318 | 2766 | 106

## Slide 12
  On the sewer side, WASCO provides sewer connections and emptying services for Conservancy tanks and VIP latrines
  The company has 2141 sewer connections classified into
    Domestic and
    Non-domestic
Chart: Sewer Connections
| Domestic | Non-domestic
 | 1149 | 992

## Slide 13
  WASCO also provides emptying services to
  12, 000 Customers mainly in Maseru

## Slide 14
  Out of a clientele of 44318 domestic water connections, only 1149 (2.6%) domestic customers are connected to the sewer
  In response to this disparity in services and taking the challenges of urbanisation into account
  WASCO conceptualised the Maseru Wastewater project and sought and received funding from the EU-WF, EIB and the GOL for implementation of this project
  The total project cost is estimated at Euro 28.6million (approx. M286 million)

## Slide 15
The objectives of this project are:
    To contribute towards Government of Lesotho efforts to achieve the MDGs
    To reduce the pollution of water resources
    To contribute to the reduction of water-related diseases in urban Maseru

## Slide 16
Project Components
  There are 6 services contracts
    ESIA
    TA to PIU
    Design and construction supervision
    Mid-term review
    Development of the Urban Sanitation Infrastructure Master plan
    End – Term Review

## Slide 17
Project Components cont’d
  3 Works Contracts
    Network contract –
      app. 132 km of sewer network, three pump stations
    WWTW
      7Ml/day AS treatment plant, the ultimate capacity of the plant will be 22Ml/day
    Provision of on-site sanitation facilities
      conversion of existing VIP latrines into water closets
      Construction of new water closets
      Construction of VIP latrines

## Slide 18
The project covers the following areas
  Mabote
  Khubetsoana
  Maqalika
  Ntsirele
  MASOWE

## Slide 19
Target Groups
  For 7200 (36,000 P.E.) households, classified as high income households, sewer connections have been conceptualised
  For 5600 (28,000 P.E) households, classified as middle income households, water closets are to be provided and
  For 7200 (36,000 P.E.) classified as low income households, VIP latrines are to be provided

## Slide 20
Sewage collected from the reticulated areas will be treated in a treatment plant under construction at Agricultural College

## Slide 21
Project Challenges
  Since project conception in 2004, the population of Maseru is double the projected population due to substantial increase in migration from the rural to the urban areas
  The pipeline routes have had to be changed due obstructions that did not exist at the time of preparing the preliminary and detailed designs
  The prices of materials have increased substantially resulting in the project scope being reduced to almost half of the original scope

## Slide 22
Challenges cont’d
  Possible shortfall in financing due to the exchange rate risk - there maybe need to raise additional funding to bridge the shortfall
  The project has become a major PR challenge for WASCO due to complaints from the public which include :
    disruption of services
    access to individual plots
    Demand for compensation for damaged fences/boundary walls/ crops etc.
  Concurrent implementation of projects in one area (roads and sewer network)

## Slide 23
The Way forward for Urban sanitation in Lesotho
  Immediately, we have to raise capital for implementation of the rest of the MWWP scope
  In the near future
    As part of the MWWP, an Urban sanitation infrastructure master plan will be developed.
    Allocation of resources to bridge the gap between water supply and sanitation provision
    Pacing service delivery to match development of settlements

## Slide 24
Key questions to be addressed by National Sanitation Policy
  How do we ensure that services (water supply, sanitation and other services) are in place before settlements are established
  How do we provide services to the settlements that are already established taking into account the current and future challenges
  How do we ensure that where sanitation infrastructure is in place that households connect to the sewer network
    WASCO for its part,
      has ensured that a connection is left for each household 0.5m from the plot boundary
      provides connection on credit allowing up to 36months to pay
    What else can be done?

## Slide 25
  For water supply basic service level is 30lcd, policy has to define the basic service level for sanitation
  We say, every Mosotho has a right to the basic level of service but we should ask ourselves ….
    How do we fulfil that right?
    Who is responsible for fulfilling that right?

## Slide 26
Thank you